BBK MPLS Requirements

BGP

       EBGP is to be used as the CE-PE protocol. 
       AS_OVERIDE is to be used within your MPLS cloud to allow us to use the same AS number at all our sites. 
       AS number to be used 
       BGP communities are to be propagated though MPLS cloud to our CE’s. 
       BGP timers for better convergence will be tuned after migrating sites and stability has been proven. 
       Any single homed sites will use static routing. 
       IP addressing for CE-PE links to be provide by BBK.

General

       The point-to-point links between the primary and DR sites should be diversely routed from the MPLS cloud link.

       For each link different SP termination units should be provided. Two links are not use the same termination unit.

       Could we see the configuration of the PE devices you will use? 
       We will provide 7 x 3845 for your POP PE routers, which interface/IOS ect should be included? Could you provide Sawe with the spec so as the order can be place promptly for the equipment?

       Interface terminations are v.35 for MPLS and point-to-point link? 
       Links will have PPP encapsulation.

QOS for Voice/Apps

       SP’s should use MPLS DiffServe short pipe mode, adhering to the attached five-class PE marking model.