berbee side 7206

pseudowire-class class10

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

!

pseudowire-class class41

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

!

pseudowire-class class42

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

!

pseudowire-class class100

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

!

pseudowire-class class70

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

!

pseudowire-class class111

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

interface Loopback0

ip address 10.2.0.20 255.255.255.255

!

interface Loopback1

description l2tpv3 route point

ip address 10.2.200.2 255.255.255.255

interface GigabitEthernet0/1

bandwidth 100000

ip address 10.2.0.179 255.255.255.248

ip ospf authentication message-digest

ip ospf message-digest-key 76 md5 7 141211060F493B26742D77

duplex full

speed 1000

media-type rj45

negotiation auto

service-policy output WAN-EDGE

!

interface FastEthernet0/2

no ip address

shutdown

duplex auto

speed auto

!

interface GigabitEthernet0/2

description Berbee WAN and LAN Trunk

no ip address

duplex auto

speed auto

media-type rj45

negotiation auto

!

interface GigabitEthernet0/2.1

description WAN Subnet vlan 37

encapsulation dot1Q 37

ip address 10.2.0.146 255.255.255.240

!

interface GigabitEthernet0/2.2

description Production VLAN 10

encapsulation dot1Q 10

xconnect 10.2.200.1 123 pw-class class10

!

interface GigabitEthernet0/2.3

description Prod DMZ1 VLAN 41

encapsulation dot1Q 41

xconnect 10.2.200.1 456 pw-class class41

!

interface GigabitEthernet0/2.4

--More--          description Prod DMZ2 VLAN 42

encapsulation dot1Q 42

xconnect 10.2.200.1 789 pw-class class42

!

interface GigabitEthernet0/2.5

description Prod DMZ2 VLAN 100

encapsulation dot1Q 100

xconnect 10.2.200.1 100 pw-class class100

!

interface GigabitEthernet0/2.6

description Prod DMZ2 VLAN 70

encapsulation dot1Q 70

xconnect 10.2.200.1 170 pw-class class70

!

interface GigabitEthernet0/2.7

description Prod DMZ2 VLAN 111

encapsulation dot1Q 111

xconnect 10.2.200.1 111 pw-class class111

!

interface GigabitEthernet0/3

bandwidth 200000

description - 200M QMOE L2TPV3 link

ip address 10.2.0.49 255.255.255.240

duplex auto

speed auto

media-type rj45

negotiation auto

VISI 7206

pseudowire-class class10

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

!

pseudowire-class class41

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

!

pseudowire-class class42

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

!

pseudowire-class class100

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

!

pseudowire-class class70

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

!

pseudowire-class class111

encapsulation l2tpv3

ip local interface Loopback1

ip pmtu max 1400

interface Loopback0

ip address 10.2.0.19 255.255.255.255

!

interface Loopback1

description l2tpv3 route point

ip address 10.2.200.1 255.255.255.255

!

interface Loopback2

description l2tpv3 route point to St Paul

ip address 10.2.200.4 255.255.255.255

!

interface GigabitEthernet0/1

description QMOE

bandwidth 100000

ip address 10.2.0.178 255.255.255.248

ip access-group 130 in

ip ospf authentication message-digest

ip ospf message-digest-key 76 md5 7 110C1A08145F1A01542F6F

duplex full

speed 1000

media-type rj45

negotiation auto

service-policy output WAN-EDGE

!

interface FastEthernet0/2

no ip address

shutdown

duplex auto

speed auto

!

interface GigabitEthernet0/2

description VISI WAN and LAN Trunk

no ip address

duplex auto

speed auto

media-type rj45

negotiation auto

!

interface GigabitEthernet0/2.1

description WAN Subnet vlan 37

encapsulation dot1Q 37

ip address 10.2.0.193 255.255.255.240

!

--More--         interface GigabitEthernet0/2.2

description Production VLAN 10

encapsulation dot1Q 10

xconnect 10.2.200.2 123 pw-class class10

!

interface GigabitEthernet0/2.3

description Prod DMZ1 VLAN 41

encapsulation dot1Q 41

xconnect 10.2.200.2 456 pw-class class41

!

interface GigabitEthernet0/2.4

description Prod DMZ2 VLAN 42

encapsulation dot1Q 42

xconnect 10.2.200.2 789 pw-class class42

!

interface GigabitEthernet0/2.5

description Prod DMZ2 VLAN 100

encapsulation dot1Q 100

xconnect 10.2.200.2 100 pw-class class100

!

interface GigabitEthernet0/2.6

description Prod DMZ2 VLAN 70

encapsulation dot1Q 70

xconnect 10.2.200.2 170 pw-class class70

!

interface GigabitEthernet0/2.7

description Prod DMZ2 VLAN 111

encapsulation dot1Q 111

xconnect 10.2.200.2 111 pw-class class111

!

interface GigabitEthernet0/2.9

encapsulation dot1Q 40

xconnect 10.2.200.3 140 pw-class class40

!

interface GigabitEthernet0/3

bandwidth 200000

description - 200M QMOE L2TPV3 link

ip address 10.2.0.50 255.255.255.240

duplex auto

speed auto

media-type rj45

negotiation auto