Cisco Adaptive Security Appliance Software Version 7.0(4)12

Device Manager Version 5.0(4)

Compiled on Mon 20-Mar-06 14:14 by builders

System image file is "disk0:/asa704-12-k8.bin"

Config file at boot was "startup-config"

wotif-vpn1 up 138 days 0 hours

Hardware:   ASA5510, 256 MB RAM, CPU Pentium 4 Celeron 1600 MHz

Internal ATA Compact Flash, 256MB

BIOS Flash M50FW080 @ 0xffe00000, 1024KB

Encryption hardware device : Cisco ASA-55x0 on-board accelerator (revision 0x0)

Boot microcode   : CNlite-MC-Boot-Cisco-1.2

SSL/IKE microcode: CNlite-MC-IPSEC-Admin-3.03

IPSec microcode  : CNlite-MC-IPSECm-MAIN-2.04

0: Ext: Ethernet0/0         : address is 0016.c79f.7e7e, irq 9

1: Ext: Ethernet0/1         : address is 0016.c79f.7e7f, irq 9

2: Ext: Ethernet0/2         : address is 0016.c79f.7e80, irq 9

3: Ext: Not licensed        : irq 9

4: Ext: Management0/0       : address is 0016.c79f.7e82, irq 11

5: Int: Not licensed        : irq 11

6: Int: Not licensed        : irq 5

<--- More --->

Licensed features for this platform:

Maximum Physical Interfaces : 4

Maximum VLANs               : 0

Inside Hosts                : Unlimited

Failover                    : Disabled

VPN-DES                     : Enabled

VPN-3DES-AES                : Enabled

Security Contexts           : 0

GTP/GPRS                    : Disabled

VPN Peers                   : 50

This platform has a Base license.

Serial Number: JMX1017K0YH

Running Activation Key: 0xb6370160 0x8879503c 0xcc5015f4 0xb414a038 0xcb30e9ba

Configuration register is 0x1

Configuration last modified by pauls at 11:04:20.002 UTC Wed Nov 22 2006

------------------ show clock ------------------

15:00:48.002 UTC Wed Nov 22 2006

------------------ show memory ------------------

<--- More --->

Free memory:       205431104 bytes (77%)

Used memory:        63004352 bytes (23%)

-------------     ----------------

Total memory:      268435456 bytes (100%)

------------------ show conn count ------------------

239 in use, 307 most used

------------------ show xlate count ------------------

8 in use, 11 most used

------------------ show blocks ------------------

SIZE    MAX    LOW    CNT

4    300    297    299

80    100     96    100

256    612    581    612

1550   9251   7624   7706

2048    100     99    100

2560     40     40     40

4096     30     29     30

<--- More --->                8192     60     59     60

16384    102    102    102

65536     10     10     10

------------------ show blocks queue history detail ------------------

History buffer memory usage: 2136 bytes (default)

------------------ show interface ------------------

Interface Ethernet0/0 "inside", is up, line protocol is up

Hardware is i82546GB rev03, BW 100 Mbps

Full-Duplex(Full-duplex), 100 Mbps(100 Mbps)

MAC address 0016.c79f.7e7e, MTU 1500

IP address 10.6.241.155, subnet mask 255.255.255.240

90510993 packets input, 107754072332 bytes, 0 no buffer

Received 190 broadcasts, 0 runts, 0 giants

0 input errors, 0 CRC, 0 frame, 0 overrun, 0 ignored, 0 abort

0 L2 decode drops

63791349 packets output, 7585769640 bytes, 0 underruns

0 output errors, 655 collisions

293 late collisions, 2119 deferred

input queue (curr/max blocks): hardware (0/0) software (0/0)

output queue (curr/max blocks): hardware (0/31) software (0/0)

<--- More --->                Traffic Statistics for "inside":

90510993 packets input, 106116758373 bytes

63791642 packets output, 6430455008 bytes

391514 packets dropped

1 minute input rate 14 pkts/sec,  1495 bytes/sec

1 minute output rate 19 pkts/sec,  2219 bytes/sec

1 minute drop rate, 0 pkts/sec

5 minute input rate 5 pkts/sec,  858 bytes/sec

5 minute output rate 10 pkts/sec,  1359 bytes/sec

5 minute drop rate, 0 pkts/sec

Control Point Interface States:

Interface number is 1

Interface config status is active

Interface state is active

Interface Ethernet0/1 "outside", is up, line protocol is up

Hardware is i82546GB rev03, BW 100 Mbps

Full-Duplex(Full-duplex), 100 Mbps(100 Mbps)

MAC address 0016.c79f.7e7f, MTU 1500

IP address 202.58.53.181, subnet mask 255.255.255.192

73922511 packets input, 10676280926 bytes, 0 no buffer

Received 14232233 broadcasts, 0 runts, 0 giants

0 input errors, 0 CRC, 0 frame, 0 overrun, 0 ignored, 0 abort

0 L2 decode drops

90336923 packets output, 112515304173 bytes, 0 underruns

<--- More --->              	0 output errors, 1308 collisions

3178 late collisions, 6388 deferred

input queue (curr/max blocks): hardware (0/0) software (0/0)

output queue (curr/max blocks): hardware (0/60) software (0/0)

Traffic Statistics for "outside":

73922508 packets input, 9344576677 bytes

90340101 packets output, 110891987217 bytes

70396 packets dropped

1 minute input rate 21 pkts/sec,  2668 bytes/sec

1 minute output rate 16 pkts/sec,  3058 bytes/sec

1 minute drop rate, 0 pkts/sec

5 minute input rate 10 pkts/sec,  1357 bytes/sec

5 minute output rate 7 pkts/sec,  1840 bytes/sec

5 minute drop rate, 0 pkts/sec

Control Point Interface States:

Interface number is 2

Interface config status is active

Interface state is active

Interface Ethernet0/2 "", is administratively down, line protocol is down

Hardware is i82546GB rev03, BW 100 Mbps

Auto-Duplex, Auto-Speed

Available but not configured via nameif

MAC address 0016.c79f.7e80, MTU not set

IP address unassigned

<--- More --->              	0 packets input, 0 bytes, 0 no buffer

Received 0 broadcasts, 0 runts, 0 giants

0 input errors, 0 CRC, 0 frame, 0 overrun, 0 ignored, 0 abort

0 L2 decode drops

0 packets output, 0 bytes, 0 underruns

0 output errors, 0 collisions

0 late collisions, 0 deferred

input queue (curr/max blocks): hardware (0/0) software (0/0)

output queue (curr/max blocks): hardware (0/0) software (0/0)

Control Point Interface States:

Interface number is unassigned

Interface Management0/0 "", is administratively down, line protocol is down

Hardware is i82557, BW 100 Mbps

Auto-Duplex, Auto-Speed

Available but not configured via nameif

MAC address 0016.c79f.7e82, MTU not set

IP address unassigned

0 packets input, 0 bytes, 0 no buffer

Received 0 broadcasts, 0 runts, 0 giants

0 input errors, 0 CRC, 0 frame, 0 overrun, 0 ignored, 0 abort

0 L2 decode drops

0 packets output, 0 bytes, 0 underruns

0 output errors, 0 collisions, 0 interface resets

0 babbles, 0 late collisions, 0 deferred

<--- More --->              	0 lost carrier, 0 no carrier

input queue (curr/max blocks): hardware (128/128) software (0/0)

output queue (curr/max blocks): hardware (1/0) software (0/0)

Control Point Interface States:

Interface number is unassigned

------------------ show cpu usage ------------------

CPU utilization for 5 seconds = 2%; 1 minute: 0%; 5 minutes: 0%

------------------ show process ------------------

PC       SP       STATE       Runtime    SBASE     Stack Process

Lwe 00105e4d 0115a860 00e6d0f0          0 011588d8 8072/8192 block_diag

Mrd 0020088a 0128eae0 00e6d158    2582207 0128ab98 11196/16384 Dispatch Unit

Mwe 003ba47d 01293b70 00e6d0a8          0 01291bf8 7684/8192 CF OIR

Mwe 00116961 01919cb8 00e6d0a8          0 01917d40 7788/8192 Reload Control Thread

Mwe 0011ac42 01922888 00e6eef0         98 01920940 5664/8192 aaa

Mwe 00137872 01927340 00e6f718          0 01925408 7644/8192 CMGR Server Process

Mwe 00137dd5 019294a0 00e6d0a8          0 01927528 7960/8192 CMGR Timer Process

Lwe 001ffe12 01933a40 00e77c38         12 01931ac8 5612/8192 dbgtrace

Msi 00422a57 01937c80 00e6d0a8      12078 01935d08 7700/8192 557mcfix

Msi 00422a01 01939da0 00e6d0a8          6 01937e28 7792/8192 557statspoll

<--- More --->              Mwe 00c2fe75 0194a648 00e6d0a8          0 019486c0 7804/8192 Chunk Manager

Msi 00767896 01953a38 00e6d0a8      29560 01951ad0 7684/8192 PIX Garbage Collector

Lsi 00afd585 01955b78 00e6d0a8       2361 01953bf0 7444/8192 route_process

Mwe 00756711 0195e820 00def8f0         18 0195c8a8 7432/8192 IP Address Assign

Mwe 00945921 019636a0 00df9e08          0 01961728 8056/8192 QoS Support Module

Mwe 007c4789 019657f8 00df067c          0 01963880 8056/8192 Client Update Task

Lwe 00c4c489 019680d0 00e6d0a8    6446166 01966158 7576/8192 Checkheaps

Mwe 0098386d 0196e420 00e6d0a8       5064 0196c4b8 7084/8192 Session Manager

Mwe 00a85795 01979118 02e5fc70          8 01975230 15620/16384 uauth

Mwe 00a20ebd 0197b280 00e0e830          0 01979308 7308/8192 Uauth_Proxy

Mwe 00a81545 0197f490 00e10bf0          0 0197d548 7660/8192 SMTP

Mwe 00a71b2d 019815c0 00e105c8     434165 0197f668 4756/8192 Logger

Mwe 00a72fe9 01983700 00e6d0a8          0 01981788 7292/8192 Thread Logger

Mwe 00b79443 0198fdb0 00e3b228          0 0198de48 6956/8192 vpnlb_thread

Msi 004e1ac3 01948518 00e6d0a8      25764 019465a0 7324/8192 arp_timer

Mwe 004eb999 0192d6d0 00e86098          0 0192b768 7964/8192 arp_forward_thread

Msi 00a87c23 02133170 00e6d0a8       8198 02131208 5596/8192 tcp_fast

Msi 00a879f7 02135188 00e6d0a8       3817 02133230 5500/8192 tcp_slow

Mwe 00a97e0b 021453a0 00e11780          0 02143438 8040/8192 udp_timer

Mwe 00185289 0197d3b0 00e6d0a8          0 0197b428 7976/8192 CTCP Timer process

Mwe 0019a050 02d9e5c0 019442c0        912 02d9c648 5004/8192 IPsec message handler

Msi 001a97b5 02da05d8 00e6d0a8     111927 02d9e670 6340/8192 CTM message handler

Mwe 00b2a015 02da26e8 00e6d0a8          0 02da0790 7928/8192 L2TP data daemon

Mwe 00b29e05 02da4818 00e6d0a8          0 02da28b0 7944/8192 L2TP mgmt daemon

<--- More --->              Mwe 00b13a87 02ddcb08 00e35fb8       7200 02dd8ba0 16024/16384 ppp_timer_thread

Msi 00b79e4e 02ddec08 00e6d0a8      39495 02ddccc0 7652/8192 vpnlb_timer_thread

Mwe 006fe9fd 02df3d70 00e6d0a8      25623 02defe08 15152/16384 IP Background

Mwe 001f92f5 02e518f0 00dc92c0       2469 02e31998 123924/131072 tmatch compile thread

Mwe 0088d2bd 02f11948 00e6d0a8          0 02f0d9c0 15996/16384 Crypto PKI RECV

Mwe 0089306d 02f13a58 00e6d0a8          0 02f11ae0 7788/8192 Crypto CA

Lsi 0077cd29 02f61130 00e6d0a8        542 02f5f1b8 7736/8192 uauth_urlb clean

Lwe 00761c4d 03117a80 00e6d0a8      13172 03115b08 7144/8192 pm_timer_thread

Mwe 00476e41 0311a858 00e6d0a8      97688 031188e0 7684/8192 IKE Timekeeper

Mwe 00469295 0311fd28 00de3dc8     274774 0311c0d0 10940/16384 IKE Daemon

Mwe 00a2d97d 03122e28 00e0fdb0          0 03120eb0 8056/8192 RADIUS Proxy Event Daemon

Mwe 00a01adc 03124dd8 031727f0         62 03122fd0 7244/8192 RADIUS Proxy Listener

Mwe 00a2f899 03127078 00e6d0a8          0 031250f0 7976/8192 RADIUS Proxy Time Keeper

Mwe 00209977 03164fd0 00ca1040      26519 0315d698 28604/32768 ci/console

Csi 007983ed 03167720 00e6d0a8     339945 031657b8 7116/8192 update_cpu_usage

Msi 00798be1 0316d8b0 00e6d0a8      94738 0316b9f8 6196/8192 NIC status poll

Mwe 00b5112c 03179e30 00e3a404          0 03177ed8 8024/8192 vpnfo_thread_msg

Msi 00b5efcb 0317be58 00e6d0a8      14418 03179f00 7668/8192 vpnfo_thread_timer

Mwe 00b5bb0b 0317de80 00e3a518          0 0317bf28 8024/8192 vpnfo_thread_sync

Msi 00b5e8c4 0317ffb0 00e6d0a8      64752 0317e048 7684/8192 vpnfo_thread_unsent

Mwe 004d9f05 031a2120 00e862a0     103572 031a01b8 7456/8192 IP Thread

Mwe 004df909 031a4158 00e86260     235543 031a21e0 5900/8192 ARP Thread

Mwe 00427555 031a6180 00e86108       8499 031a4208 5780/8192 icmp_thread

Mwe 00a97828 031a80c8 02143254          0 031a6230 7832/8192 riprx

<--- More --->              Msi 009610e1 031aa1d0 00e6d0a8       1461 031a8258 7500/8192 riptx

Mwe 00a97e63 031ac1d8 00e6d0a8       3463 031aa280 7772/8192 udp_thread

Mwe 00a88161 031ae100 00e86298      14790 031ac2a8 3884/8192 tcp_thread

Mwe 00a85bb7 0350e178 038cdf58        199 0350c2c0 7272/8192 listen/https

Mwe 0028510e 035122f0 00e6d0a8       6579 0350e398 12988/16384 emweb/https

Mwe 0027fa01 0381eed8 00e6d0a8       2423 0381cf60 7584/8192 Timekeeper

Mwe 00a01adc 03847b78 031c72e8      14847 03845d70 7320/8192 IKE Receiver

Mwe 00a85bb7 03895cb0 0318c850         46 03893e58 7332/8192 listen/ssh

Mwe 00a455e1 038fad58 00e6d0a8         12 038f8de0 5324/8192 ssh/timer

Mwe 0073d9d8 03a7bc28 03d1f6f4      32099 03a74290 28156/32768 accept/http

Mwe 0073c4f1 03930f68 00e6d0a8      23257 03929390 28540/32768 accept/http

Mwe 0092a918 03cc7650 00ef2d08      21514 03cc56f8 7828/8192 qos_metric_daemon

M*  00a3c9b1 0009feec 00e6d158      39512 03c847b0 8868/16384 ssh

Mwe 00a97828 03c712d8 02142ef8      14870 03c6fa40 4480/8192 snmp

-     -        -         -    11906850696    -         -     scheduler

-     -        -         -   11925470656    -         -     total elapsed

------------------ show failover ------------------

ERROR: Command requires failover license

------------------ show traffic ------------------

inside:

<--- More --->              	received (in 3334885.328 secs):

90510994 packets	106116758717 bytes

0 pkts/sec	31001 bytes/sec

transmitted (in 3334885.328 secs):

63791646 packets	6430455492 bytes

1 pkts/sec	1000 bytes/sec

1 minute input rate 14 pkts/sec,  1495 bytes/sec

1 minute output rate 19 pkts/sec,  2219 bytes/sec

1 minute drop rate, 0 pkts/sec

5 minute input rate 5 pkts/sec,  858 bytes/sec

5 minute output rate 10 pkts/sec,  1359 bytes/sec

5 minute drop rate, 0 pkts/sec

outside:

received (in 3334885.338 secs):

73922523 packets	9344577443 bytes

0 pkts/sec	2001 bytes/sec

transmitted (in 3334885.338 secs):

90340127 packets	110892001446 bytes

0 pkts/sec	33000 bytes/sec

1 minute input rate 21 pkts/sec,  2668 bytes/sec

1 minute output rate 16 pkts/sec,  3058 bytes/sec

1 minute drop rate, 0 pkts/sec

5 minute input rate 10 pkts/sec,  1357 bytes/sec

5 minute output rate 7 pkts/sec,  1840 bytes/sec

<--- More --->                    5 minute drop rate, 0 pkts/sec

----------------------------------------

Aggregated Traffic on Physical Interface

----------------------------------------

Ethernet0/0:

received (in 3334885.358 secs):

90510994 packets	107754072694 bytes

0 pkts/sec	32000 bytes/sec

transmitted (in 3334885.358 secs):

63791353 packets	7585770196 bytes

1 pkts/sec	2000 bytes/sec

1 minute input rate 14 pkts/sec,  1495 bytes/sec

1 minute output rate 19 pkts/sec,  2219 bytes/sec

1 minute drop rate, 0 pkts/sec

5 minute input rate 5 pkts/sec,  858 bytes/sec

5 minute output rate 10 pkts/sec,  1359 bytes/sec

5 minute drop rate, 0 pkts/sec

Ethernet0/1:

received (in 3334885.368 secs):

73922528 packets	10676282162 bytes

0 pkts/sec	3000 bytes/sec

transmitted (in 3334885.368 secs):

90336953 packets	112515320882 bytes

<--- More --->              		0 pkts/sec	33000 bytes/sec

1 minute input rate 21 pkts/sec,  2668 bytes/sec

1 minute output rate 16 pkts/sec,  3058 bytes/sec

1 minute drop rate, 0 pkts/sec

5 minute input rate 10 pkts/sec,  1357 bytes/sec

5 minute output rate 7 pkts/sec,  1840 bytes/sec

5 minute drop rate, 0 pkts/sec

Ethernet0/2:

received (in 3334886.118 secs):

0 packets	0 bytes

0 pkts/sec	0 bytes/sec

transmitted (in 3334886.118 secs):

0 packets	0 bytes

0 pkts/sec	0 bytes/sec

1 minute input rate 0 pkts/sec,  0 bytes/sec

1 minute output rate 0 pkts/sec,  0 bytes/sec

1 minute drop rate, 0 pkts/sec

5 minute input rate 0 pkts/sec,  0 bytes/sec

5 minute output rate 0 pkts/sec,  0 bytes/sec

5 minute drop rate, 0 pkts/sec

Management0/0:

received (in 3334886.128 secs):

0 packets	0 bytes

0 pkts/sec	0 bytes/sec

<--- More --->              	transmitted (in 3334886.128 secs):

0 packets	0 bytes

0 pkts/sec	0 bytes/sec

1 minute input rate 0 pkts/sec,  0 bytes/sec

1 minute output rate 0 pkts/sec,  0 bytes/sec

1 minute drop rate, 0 pkts/sec

5 minute input rate 0 pkts/sec,  0 bytes/sec

5 minute output rate 0 pkts/sec,  0 bytes/sec

5 minute drop rate, 0 pkts/sec

------------------ show perfmon ------------------

PERFMON STATS:    Current      Average

Xlates               0/s          0/s

Connections          2/s          0/s

TCP Conns            0/s          0/s

UDP Conns            0/s          0/s

URL Access           0/s          0/s

URL Server Req       0/s          0/s

TCP Fixup            0/s          0/s

TCP Intercept        0/s          0/s

HTTP Fixup           0/s          0/s

FTP Fixup            0/s          0/s

<--- More --->              AAA Authen           0/s          0/s

AAA Author           0/s          0/s

AAA Account          0/s          0/s

------------------ show counters ------------------

Protocol     Counter                     Value   Context

IP           IN_PKTS                15303858   Summary

IP           OUT_PKTS               95162019   Summary

IP           OUT_DROP_DWN                  3   Summary

IP           TO_ARP                 14235611   Summary

IP           TO_UDP                   407894   Summary

IP           TO_ICMP                  243589   Summary

IP           TO_TCP                   416732   Summary

TCP          IN_PKTS                  416731   Summary

TCP          OUT_PKTS                 537921   Summary

TCP          RCV_GOOD                  75494   Summary

TCP          NO_APP                       18   Summary

TCP          DROP_NRST                   122   Summary

TCP          SESS_CTOD                    36   Summary

TCP          CONN_RST1                   189   Summary

TCP          CONN_RST2                   287   Summary

TCP          DROP_UNACC                   10   Summary

TCP          DROP_IGNORE2                  1   Summary

<--- More --->              TCP          DROP_IGNORE3               1316   Summary

TCP          DROP_IGNORE4             153127   Summary

TCP          OUT_CLSD                   1386   Summary

TCP          HASH_ADD                   2535   Summary

TCP          HASH_MISS                  2675   Summary

TCP          SND_ACK                   78096   Summary

TCP          RCV_ACK                  334106   Summary

TCP          RCV_ACK_NEST                601   Summary

UDP          IN_PKTS                  407894   Summary

UDP          OUT_PKTS                4799252   Summary

UDP          BD_CKSUM                      2   Summary

ICMP         IN_PKTS                  243589   Summary

ICMP         OUT_PKTS                 191952   Summary

ICMP         DROP_IGNORE                  10   Summary

ICMP         PORT_UNREACH                121   Summary

SSL          HANDSHAKE_START            1671   Summary

SSL          HANDSHAKE_DONE             1671   Summary

SSL          HANDSHAKE_FAILURE          1858   Summary

SSL          OPEN_SERVER                1671   Summary

SSL          CLOSE_CALL                 1669   Summary

SSL          NEW_CTX                       1   Summary

SSL          WRITE_CALL               375466   Summary

SSL          TCP_ERR_READ                 20   Summary

SSL          NEW_CONN                   1671   Summary

<--- More --->              SSL          GET_PKT                    8522   Summary

------------------ show history ------------------

login

show lg asdm

show log asdm

show tech

------------------ show firewall ------------------

Firewall mode: Router

------------------ show running-config ------------------

: Saved

:

ASA Version 7.0(4)12

!

hostname wotif-vpn1

domain-name default.domain.invalid

enable password <removed>

names

!

<--- More --->              interface Ethernet0/0

speed 100

duplex full

nameif inside

security-level 100

ip address 10.6.241.155 255.255.255.240

!

interface Ethernet0/1

speed 100

duplex full

nameif outside

security-level 0

ip address 202.58.53.181 255.255.255.192

!

interface Ethernet0/2

shutdown

no nameif

no security-level

no ip address

!

interface Management0/0

shutdown

no nameif

no security-level

<--- More --->               no ip address

management-only

!

passwd <removed>

ftp mode passive

same-security-traffic permit inter-interface

same-security-traffic permit intra-interface

access-list allow_management extended permit tcp any any log

access-list allow_management extended permit icmp any any log

access-list allow_management extended permit ip 10.5.0.0 255.255.0.0 10.50.50.0 255.255.255

.0

access-list allow_management extended permit ip host 10.6.241.16 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.1 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.2 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.3 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.4 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.5 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.17 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.18 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.19 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.20 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.32 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.33 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.35 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.249.3 10.0.0.0 255.255.0.0

<--- More --->              access-list allow_management extended permit ip host 10.6.249.4 10.0.0.0 255.255.0.0

access-list allow_management extended permit ip host 10.6.241.6 10.0.0.0 255.255.0.0

access-list inside_nat0_outbound extended permit ip 10.6.0.0 255.255.0.0 10.50.50.0 255.255

.255.0

access-list inside_nat0_outbound extended permit ip 10.6.241.0 255.255.255.128 10.1.9.0 255

.255.255.240

access-list inside_nat0_outbound extended permit ip 10.5.0.0 255.255.0.0 10.50.50.0 255.255

.255.0

access-list inside_nat0_outbound extended permit ip any 10.1.9.16 255.255.255.248

access-list inside_nat0_outbound extended permit ip 10.6.0.0 255.255.0.0 10.1.9.0 255.255.2

55.240

access-list inside_nat0_outbound extended permit ip any 10.1.9.0 255.255.255.240

access-list inside_nat0_outbound extended permit ip host 10.6.241.1 10.1.9.16 255.255.255.2

48

access-list inside_nat0_outbound extended permit ip host 10.6.241.2 10.1.9.16 255.255.255.2

48

access-list inside_nat0_outbound extended permit ip 10.6.0.0 255.255.0.0 10.1.9.16 255.255.

255.248

access-list inside_nat0_outbound extended permit ip host 10.6.241.16 10.0.0.0 255.255.0.0

access-list inside_nat0_outbound extended permit ip 10.6.241.0 255.255.255.128 host 10.0.2.

27

access-list inside_nat0_outbound extended permit ip 10.6.249.0 255.255.255.0 host 10.0.2.27

access-list inside_nat0_outbound extended permit ip 10.6.241.0 255.255.255.128 10.0.0.0 255

.255.0.0

access-list inside_nat0_outbound extended permit ip 10.6.249.0 255.255.255.0 10.0.0.0 255.2

55.0.0

access-list outside_cryptomap_20 extended permit ip 10.6.0.0 255.255.0.0 10.50.50.0 255.255

.255.0

access-list outside_cryptomap_20 extended permit ip 10.5.0.0 255.255.0.0 10.50.50.0 255.255

.255.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.16 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.1 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.2 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.3 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.4 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.5 10.0.0.0 255.255.0.0

<--- More --->              access-list outside_cryptomap_20 extended permit ip host 10.6.241.17 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.18 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.19 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.20 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.32 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.33 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.35 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.249.3 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.249.4 10.0.0.0 255.255.0.0

access-list outside_cryptomap_20 extended permit ip host 10.6.241.6 10.0.0.0 255.255.0.0

access-list inside_access_out extended permit tcp any any log

access-list inside_access_out extended permit icmp any any log

access-list outside_cryptomap_dyn_20 extended permit ip 10.6.241.0 255.255.255.128 10.1.9.0

255.255.255.240

access-list wotif-redrock_splitTunnelAcl standard permit host 10.6.241.32

access-list wotif-redrock_splitTunnelAcl standard permit host 10.6.241.33

access-list outside_cryptomap_dyn_40 extended permit ip any 10.1.9.16 255.255.255.248

access-list wotif_splitTunnelAcl standard permit 10.6.0.0 255.255.0.0

access-list outside_cryptomap_dyn_60 extended permit ip 10.6.0.0 255.255.0.0 10.1.9.0 255.2

55.255.240

access-list wotif-user_splitTunnelAcl standard permit 10.6.0.0 255.255.0.0

access-list outside_cryptomap_dyn_80 extended permit ip any 10.1.9.0 255.255.255.240

access-list hostsworks_splitTunnelAcl standard permit any

access-list outside_cryptomap_dyn_100 extended permit ip any 10.1.9.0 255.255.255.240

access-list outside_cryptomap_dyn_120 extended permit ip any 10.1.9.16 255.255.255.248

access-list outside_cryptomap_dyn_140 extended permit ip any 10.1.9.0 255.255.255.240

<--- More --->              access-list outside_cryptomap_dyn_160 extended permit ip any 10.1.9.0 255.255.255.240

access-list outside_cryptomap_dyn_180 extended permit ip any 10.1.9.0 255.255.255.240

access-list outside_cryptomap_dyn_200 extended permit ip 10.6.0.0 255.255.0.0 10.1.9.0 255.

255.255.240

access-list outside_cryptomap_dyn_220 extended permit ip host 10.6.241.1 10.1.9.16 255.255.

255.248

access-list outside_cryptomap_dyn_220 extended permit ip host 10.6.241.2 10.1.9.16 255.255.

255.248

access-list outside_cryptomap_dyn_240 extended permit ip 10.6.0.0 255.255.0.0 10.1.9.16 255

.255.255.248

access-list outside_access_in extended permit ip 10.50.50.0 255.255.255.0 10.5.0.0 255.255.

0.0

pager lines 24

logging enable

logging timestamp

logging console notifications

logging monitor debugging

logging trap debugging

logging history emergencies

logging asdm debugging

logging mail debugging

logging facility 16

logging device-id ipaddress inside

logging host inside 10.5.254.9

logging debug-trace

logging permit-hostdown

mtu inside 1500

mtu outside 1500

ip local pool Wotif-users 10.1.9.1-10.1.9.14 mask 255.255.255.240

<--- More --->              ip local pool Wotif-redrock 10.1.9.17-10.1.9.22 mask 255.255.255.248

icmp permit host 10.5.32.5 inside

icmp permit any inside

icmp permit host 202.83.94.59 outside

icmp permit host 202.83.94.60 outside

icmp permit host 202.83.94.61 outside

icmp permit host 202.83.94.62 outside

icmp permit host 202.58.32.114 outside

asdm image disk0:/asdm-504.bin

no asdm history enable

arp timeout 14400

nat-control

nat (inside) 0 access-list inside_nat0_outbound

nat (inside) 0 0.0.0.0 0.0.0.0

access-group allow_management in interface inside

access-group inside_access_out out interface inside

access-group outside_access_in in interface outside

route inside 10.6.249.0 255.255.255.0 10.6.241.158 1

route inside 10.6.241.0 255.255.255.128 10.6.241.158 1

route inside 10.254.32.0 255.255.255.0 10.6.241.158 1

route inside 10.101.0.0 255.255.0.0 10.6.241.158 1

route inside 10.69.0.200 255.255.255.255 10.6.241.158 1

route inside 10.5.0.0 255.255.0.0 10.6.241.158 1

route outside 10.0.0.0 255.255.0.0 202.58.53.190 1

<--- More --->              route outside 10.50.50.0 255.255.255.0 202.58.53.190 1

route outside 0.0.0.0 0.0.0.0 202.58.53.190 1

timeout xlate 3:00:00

timeout conn 1:00:00 half-closed 0:10:00 udp 0:02:00 icmp 0:00:02

timeout sunrpc 0:10:00 h323 0:05:00 h225 1:00:00 mgcp 0:05:00

timeout mgcp-pat 0:05:00 sip 0:30:00 sip_media 0:02:00

timeout uauth 0:05:00 absolute

group-policy DfltGrpPolicy attributes

banner none

wins-server none

dns-server none

dhcp-network-scope none

vpn-access-hours none

vpn-simultaneous-logins 3

vpn-idle-timeout none

vpn-session-timeout none

vpn-filter none

vpn-tunnel-protocol IPSec webvpn

password-storage disable

ip-comp disable

re-xauth disable

group-lock none

pfs disable

ipsec-udp disable

<--- More --->               ipsec-udp-port 10000

split-tunnel-policy tunnelall

split-tunnel-network-list none

default-domain none

split-dns none

secure-unit-authentication disable

user-authentication disable

user-authentication-idle-timeout 30

ip-phone-bypass disable

leap-bypass disable

nem disable

backup-servers keep-client-config

client-firewall none

client-access-rule none

webvpn

functions url-entry

port-forward-name value Application Access

group-policy hostsworks internal

group-policy hostsworks attributes

split-tunnel-policy tunnelspecified

split-tunnel-network-list value hostsworks_splitTunnelAcl

webvpn

group-policy wotif internal

group-policy wotif attributes

<--- More --->               split-tunnel-policy tunnelspecified

split-tunnel-network-list value wotif_splitTunnelAcl

webvpn

group-policy wotif-user internal

group-policy wotif-user attributes

vpn-idle-timeout none

vpn-session-timeout none

split-tunnel-policy tunnelspecified

split-tunnel-network-list value wotif-user_splitTunnelAcl

webvpn

group-policy wotif-redrock internal

group-policy wotif-redrock attributes

split-tunnel-policy tunnelspecified

split-tunnel-network-list value wotif-redrock_splitTunnelAcl

webvpn

username ssulman password <removed> privilege 0

username ssulman attributes

vpn-group-policy wotif-user

webvpn

username pauls password <removed> privilege 15

username techtest password <removed> privilege 0

username techtest attributes

vpn-group-policy wotif-user

webvpn

<--- More --->              username lmurray password <removed> privilege 0

username lmurray attributes

vpn-group-policy wotif-user

webvpn

username swong password <removed> privilege 0

username swong attributes

vpn-group-policy wotif-user

vpn-access-hours none

vpn-simultaneous-logins 3

vpn-idle-timeout none

vpn-session-timeout none

webvpn

username support password <removed>

username awilder password <removed> privilege 0

username awilder attributes

vpn-group-policy wotif-user

webvpn

username wotif-office-qld password <removed>

username wotiftester password <removed> privilege 0

username wotiftester attributes

vpn-group-policy wotif-user

webvpn

username Wotif-redrock password <removed> privilege 0

username Wotif-redrock attributes

<--- More --->               vpn-group-policy wotif-redrock

webvpn

username pyoung password <removed> privilege 0

username pyoung attributes

vpn-group-policy wotif-user

webvpn

username kanem password <removed> privilege 15

username netmgr password <removed> privilege 15

username mandelkowg password <removed> privilege 0

username mandelkowg attributes

vpn-group-policy wotif-user

webvpn

username givers password <removed>

username givers attributes

vpn-group-policy wotif-user

webvpn

username mbaker password <removed>

username mbaker attributes

vpn-group-policy wotif-user

webvpn

aaa authentication enable console LOCAL

aaa authentication ssh console LOCAL

aaa authentication http console LOCAL

http server enable

<--- More --->              http 10.5.0.0 255.255.0.0 inside

http 202.58.62.0 255.255.255.0 outside

snmp-server host inside 10.5.0.68 community 0EjPklMsM^ udp-port 161

no snmp-server location

no snmp-server contact

snmp-server enable traps snmp authentication linkup linkdown coldstart

sysopt noproxyarp outside

crypto ipsec transform-set ESP-3DES-SHA esp-3des esp-sha-hmac

crypto dynamic-map outside_dyn_map 20 match address outside_cryptomap_dyn_20

crypto dynamic-map outside_dyn_map 20 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 40 match address outside_cryptomap_dyn_40

crypto dynamic-map outside_dyn_map 40 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 60 match address outside_cryptomap_dyn_60

crypto dynamic-map outside_dyn_map 60 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 80 match address outside_cryptomap_dyn_80

crypto dynamic-map outside_dyn_map 80 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 100 match address outside_cryptomap_dyn_100

crypto dynamic-map outside_dyn_map 100 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 120 match address outside_cryptomap_dyn_120

crypto dynamic-map outside_dyn_map 120 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 140 match address outside_cryptomap_dyn_140

crypto dynamic-map outside_dyn_map 140 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 160 match address outside_cryptomap_dyn_160

crypto dynamic-map outside_dyn_map 160 set transform-set ESP-3DES-SHA

<--- More --->              crypto dynamic-map outside_dyn_map 180 match address outside_cryptomap_dyn_180

crypto dynamic-map outside_dyn_map 180 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 200 match address outside_cryptomap_dyn_200

crypto dynamic-map outside_dyn_map 200 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 220 match address outside_cryptomap_dyn_220

crypto dynamic-map outside_dyn_map 220 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 240 match address outside_cryptomap_dyn_240

crypto dynamic-map outside_dyn_map 240 set transform-set ESP-3DES-SHA

crypto map outside_map 20 match address outside_cryptomap_20

crypto map outside_map 20 set peer 202.83.76.222

crypto map outside_map 20 set transform-set ESP-3DES-SHA

crypto map outside_map 65535 ipsec-isakmp dynamic outside_dyn_map

crypto map outside_map interface outside

isakmp identity auto

isakmp enable inside

isakmp enable outside

isakmp policy 10 authentication pre-share

isakmp policy 10 encryption 3des

isakmp policy 10 hash sha

isakmp policy 10 group 2

isakmp policy 10 lifetime 86400

tunnel-group DefaultRAGroup general-attributes

authentication-server-group none

tunnel-group 202.83.76.222 type ipsec-l2l

<--- More --->              tunnel-group 202.83.76.222 ipsec-attributes

pre-shared-key *

tunnel-group wotif-user type ipsec-ra

tunnel-group wotif-user general-attributes

address-pool Wotif-users

default-group-policy wotif-user

tunnel-group wotif-user ipsec-attributes

pre-shared-key *

tunnel-group wotif-redrock type ipsec-ra

tunnel-group wotif-redrock general-attributes

address-pool Wotif-redrock

default-group-policy wotif-redrock

tunnel-group wotif-redrock ipsec-attributes

pre-shared-key *

tunnel-group hostsworks type ipsec-ra

tunnel-group hostsworks general-attributes

address-pool Wotif-users

default-group-policy hostsworks

tunnel-group hostsworks ipsec-attributes

pre-shared-key *

no tunnel-group-map enable ou

no tunnel-group-map enable ike-id

telnet timeout 5

ssh 10.5.0.0 255.255.0.0 inside

<--- More --->              ssh 202.58.62.0 255.255.255.0 outside

ssh timeout 60

console timeout 0

!

class-map inspection_default

match default-inspection-traffic

!

!

policy-map global_policy

class inspection_default

inspect dns maximum-length 512

inspect ftp

inspect h323 h225

inspect h323 ras

inspect netbios

inspect rsh

inspect rtsp

inspect skinny

inspect esmtp

inspect sqlnet

inspect sunrpc

inspect tftp

inspect sip

inspect xdmcp

<--- More --->              !

service-policy global_policy global

Cryptochecksum:937ec41f4bcd1908409402d7a4c586f6

: end

------------------ show startup-config errors ------------------

nat 0 0.0.0.0 will be identity translated for outbound

*** Output from config line 67, "nat (inside) 0 0.0.0.0 0..."

WARNING: L2L tunnel-groups that have names which are not an IP

address may only be used if the tunnel authentication

method is Digitial Certificates and/or The peer is

configured to use Aggressive Mode

*** Output from config line 129, "tunnel-group "DR tunnel"..."

------------------ console logs ------------------

Message #1 : Message #2 : Message #3 : Message #4 : Message #5 : Message #6 : Message #7 :

Message #8 : Message #9 : Message #10 : Message #11 : Message #12 : Message #13 : Message #

14 :

Total SSMs found: 0

Message #15 :

Total NICs found: 7

Message #16 : mcwa Message #17 : i82557 Ethernet at irq 11Message #18 :   MAC: 0016.c79f.7e

82

Message #19 : mcwa Message #20 : i82557 Ethernet at irq  5Message #21 :   MAC: 0000.0001.00

01

Message #22 : i82547GI rev00 Gigabit Ethernet @ irq11 dev 1 index 05Message #23 :  MAC: 000

0.0001.0002

<--- More --->              Message #24 : i82546GB rev03 Ethernet @ irq09 dev 2 index 03Message #25 :  MAC: 0016.c79f.7

e81

Message #26 : i82546GB rev03 Ethernet @ irq09 dev 2 index 02Message #27 :  MAC: 0016.c79f.7

e80

Message #28 : i82546GB rev03 Ethernet @ irq09 dev 3 index 01Message #29 :  MAC: 0016.c79f.7

e7f

Message #30 : i82546GB rev03 Ethernet @ irq09 dev 3 index 00Message #31 :  MAC: 0016.c79f.7

e7e

Message #32 :

Licensed features for this platform:

Message #33 : Maximum Physical Interfaces : 4

Message #34 : Maximum VLANs               : 0

Message #35 : Inside Hosts                : Unlimited

Message #36 : Failover                    : Disabled

Message #37 : VPN-DES                     : Enabled

Message #38 : VPN-3DES-AES                : Enabled

Message #39 : Security Contexts           : 0

Message #40 : GTP/GPRS                    : Disabled

Message #41 : VPN Peers                   : 50

Message #42 :

This platform has a Base license.

Message #43 :

Message #44 : Encryption hardware device : Cisco ASA-55x0 on-board accelerator (revision 0x

0)

Message #45 :                              Boot microcode   : CNlite-MC-Boot-Cisco-1.2

Message #46 :                              SSL/IKE microcode: CNlite-MC-IPSEC-Admin-3.03

Message #47 :                              IPSec microcode  : CNlite-MC-IPSECm-MAIN-2.04

Message #48 :   --------------------------------------------------------------------------

Message #49 :                                  .            .

<--- More --->              Message #50 :                                  |            |

Message #51 :                                 |||          |||

Message #52 :                               .|| ||.      .|| ||.

Message #53 :                            .:||| | |||:..:||| | |||:.

Message #54 :                             C i s c o  S y s t e m s

Message #55 :   --------------------------------------------------------------------------

Message #56 :

Cisco Adaptive Security Appliance Software Version 7.0(4)12

Message #57 : Additional 1 interface(s) are disabled

Message #58 :

Message #59 :   ****************************** Warning *******************************

Message #60 :   This product contains cryptographic features and is

Message #61 :   subject to United States and local country laws

Message #62 :   governing, import, export, transfer, and use.

Message #63 :   Delivery of Cisco cryptographic products does not

Message #64 :   imply third-party authority to import, export,

Message #65 :   distribute, or use encryption. Importers, exporters,

Message #66 :   distributors and users are responsible for compliance

Message #67 :   with U.S. and local country laws. By using this

Message #68 :   product you agree to comply with applicable laws and

Message #69 :   regulations. If you are unable to comply with U.S.

Message #70 :   and local laws, return the enclosed items immediately.

Message #71 :

Message #72 :   A summary of U.S. laws governing Cisco cryptographic

<--- More --->              Message #73 :   products may be found at:

Message #74 :   http://www.cisco.com/wwl/export/crypto/tool/stqrg.html

Message #75 :

Message #76 :   If you require further assistance please contact us by

Message #77 :   sending email to export@cisco.com.

Message #78 :   ******************************* Warning *******************************

Message #79 :

Message #80 : Copyright (c) 1996-2005 by Cisco Systems, Inc.

Message #81 :                 Restricted Rights Legend

Message #82 : Use, duplication, or disclosure by the Government is

Message #83 : subject to restrictions as set forth in subparagraph

Message #84 : (c) of the Commercial Computer Software - Restricted

Message #85 : Rights clause at FAR sec. 52.227-19 and subparagraph

Message #86 : (c) (1) (ii) of the Rights in Technical Data and Computer

Message #87 : Software clause at DFARS sec. 252.227-7013.

Message #88 :                 Cisco Systems, Inc.

Message #89 :                 170 West Tasman Drive

Message #90 :                 San Jose, California 95134-1706

wotif-vpn1#