login as: cisco

cisco@61.12.8.228's password:

Type help or '?' for a list of available commands.

ciscoasa> en

Password: *****

ciscoasa# sh run

: Saved

:

ASA Version 8.0(3)6

!

hostname ciscoasa

domain-name cisco.com

enable password 2KFQnbNIdI.2KYOU encrypted

passwd 2KFQnbNIdI.2KYOU encrypted

names

!

interface Vlan1

description LAN

nameif inside

security-level 100

ip address 192.168.100.1 255.255.255.0

!

interface Vlan2

description WAN

nameif outside

security-level 0

ip address 61.12.8.228 255.255.255.240

!

interface Ethernet0/0

switchport access vlan 2

!

interface Ethernet0/1

!

interface Ethernet0/2

!

interface Ethernet0/3

!

interface Ethernet0/4

!

interface Ethernet0/5

!

interface Ethernet0/6

!

interface Ethernet0/7

!

ftp mode passive

dns domain-lookup outside

dns server-group DefaultDNS

name-server 202.56.250.6

name-server 61.12.21.34

name-server 203.196.128.4

domain-name cisco.com

same-security-traffic permit inter-interface

same-security-traffic permit intra-interface

access-list OutsideAllowedIn extended permit tcp any interface outside eq www

access-list OutsideAllowedIn extended permit tcp any interface outside eq smtp

access-list OutsideAllowedIn extended permit tcp any interface outside eq https

access-list OutsideAllowedIn extended permit tcp any interface outside eq 3389

access-list OutsideAllowedIn extended permit icmp any any

access-list inside_access_in extended permit ip any any

access-list inside_nat0_outside extended permit ip any 192.168.1.0 255.255.255.0

access-list inside_nat0_outside extended permit ip host 192.168.1.0 192.168.1.0 255.255.255.0

access-list outside_access_in extended permit ip any any

access-list cisco_splitTunnelAcl standard permit host 192.168.1.0

access-list outside_access_in_1 extended permit ip any any

access-list nonat extended permit ip 192.168.100.0 255.255.255.0 192.168.2.0 255.255.255.0

access-list 101 extended permit esp any any

access-list 101 extended permit udp any any eq isakmp

access-list 101 extended permit tcp any any eq 10000

pager lines 24

logging enable

logging buffered debugging

logging asdm informational

mtu inside 1500

mtu outside 1500

ip local pool vpnpool 192.168.2.2-192.168.2.129 mask 255.255.255.0

icmp unreachable rate-limit 1 burst-size 1

icmp permit any echo-reply outside

icmp permit any unreachable outside

icmp permit any echo outside

asdm image disk0:/asdm-603.bin

no asdm history enable

arp timeout 14400

global (outside) 1 interface

nat (inside) 0 access-list nonat

nat (inside) 1 0.0.0.0 0.0.0.0

access-group inside_access_in in interface inside

access-group outside_access_in_1 in interface outside

route outside 0.0.0.0 0.0.0.0 61.12.8.225 1

timeout xlate 3:00:00

timeout conn 1:00:00 half-closed 0:10:00 udp 0:02:00 icmp 0:00:02

timeout sunrpc 0:10:00 h323 0:05:00 h225 1:00:00 mgcp 0:05:00 mgcp-pat 0:05:00

timeout sip 0:30:00 sip_media 0:02:00 sip-invite 0:03:00 sip-disconnect 0:02:00

timeout sip-provisional-media 0:02:00 uauth 0:05:00 absolute

dynamic-access-policy-record DfltAccessPolicy

eou allow none

aaa authentication ssh console LOCAL

http server enable

http 192.168.1.0 255.255.255.0 inside

no snmp-server location

no snmp-server contact

snmp-server enable traps snmp authentication linkup linkdown coldstart

crypto ipsec transform-set ESP-3DES-SHA esp-3des esp-sha-hmac

crypto dynamic-map Outside_dyn_map 10 set transform-set ESP-3DES-SHA

crypto dynamic-map outside_dyn_map 10 set transform-set ESP-3DES-SHA

crypto map Outside_map 65535 ipsec-isakmp dynamic Outside_dyn_map

crypto map Outside_map interface outside

crypto isakmp enable outside

crypto isakmp policy 10

authentication pre-share

encryption 3des

hash sha

group 2

lifetime 86400

crypto isakmp ipsec-over-tcp port 10000

no vpn-addr-assign aaa

telnet 0.0.0.0 0.0.0.0 inside

telnet timeout 5

ssh 0.0.0.0 0.0.0.0 inside

ssh 0.0.0.0 0.0.0.0 outside

ssh timeout 5

console timeout 0

dhcpd dns 202.56.250.6

dhcpd auto_config outside

!

threat-detection basic-threat

threat-detection statistics access-list

group-policy cisco-test internal

group-policy cisco internal

group-policy cisco attributes

dns-server value 202.56.250.6

vpn-tunnel-protocol IPSec

split-tunnel-policy tunnelspecified

default-domain value test.com

user-authentication enable

username vpnuser4 password rH73Y3MkpcDD1xrq encrypted

username vpnuser5 password rH73Y3MkpcDD1xrq encrypted

username vpnuser5 attributes

service-type remote-access

username vpnuser2 password rH73Y3MkpcDD1xrq encrypted

username vpnuser2 attributes

service-type remote-access

username vpnuser3 password rH73Y3MkpcDD1xrq encrypted

username vpnuser1 password rH73Y3MkpcDD1xrq encrypted

username vpnuser1 attributes

service-type remote-access

username cisco123 password ffIRPGpDSOJh9YLq encrypted privilege 15

username cisco password 3USUcOPFUiMCO4Jk encrypted privilege 15

username choice password QpaYjfHEa2bXz.3. encrypted privilege 0

tunnel-group cisco type remote-access

tunnel-group cisco general-attributes

address-pool vpnpool

default-group-policy cisco

tunnel-group cisco ipsec-attributes

pre-shared-key *

tunnel-group cisco-test type remote-access

!

class-map inspection_default

match default-inspection-traffic

!

!

policy-map type inspect dns preset_dns_map

parameters

message-length maximum 512

policy-map global_policy

class inspection_default

inspect dns preset_dns_map

inspect ftp

inspect h323 h225

inspect h323 ras

inspect rsh

inspect rtsp

inspect esmtp

inspect sqlnet

inspect skinny

inspect sunrpc

inspect xdmcp

inspect sip

inspect netbios

inspect tftp

!

service-policy global_policy global

prompt hostname context

Cryptochecksum:b5cfee5ec5a8a7655c21265c9040f08c

: end

ciscoasa#