Hello,

how upload firmware and boot code via concole?

here how you do it

look at picutre computer IP 192.168.1.101

in this picture boot code is sx300_boot-13506.rfb

and firmware file is sx300_fw-13558.ros  firmware version 1.3.5.58

customer want you as Cisco engineer use CLI for load boot code and firmware

step 1: login to console

step 2: show version    ( you see firmware version )

step 3: show bootvar    ( show command let you see two image version in switch, ACtive* mean active image in switch, see picture 2 )

step 4: load boot code   ( select boot file from tftp server sx300_boot-13506.rfb and click copy, please look at picture 3 )

step 5: command

# copy boot tftp://192.168.1.101/sx300_boot-13506.rfb     ( all you need to do type copy boot tftp://192.168.1.101/press right button in your mouse and you will see file name show command )

!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!

now new boot code is load it!

change firmware

step 1: load firmware  ( select firmware from tftp server sx300_fw-13558.ros and click copy, Please look at picture 4 )

step 2: command

# copy tftp://192.168.1.101/sx300_fw-13558.ros image  ( all you need to do type copy tftp://192.168.1.101/press right button in your mouse and you will see file name show command )

!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!

now new firmware load

step 3: show bootvar ( look for the new firmware version in image-1 or image-2, in my case it is image-1, please look at picture 5 )

step 4: command

# boot system image-1

# wr mem

# reload

all commanf withought explane

#show version

#show bootvar

#copy boot tftp://192.168.1.101/sx300_boot-13506.rfb

#copy tftp://192.168.1.101/sx300_fw-13558.ros image

#show bootvar

#boot system image-1

#wr mem

#reload

Thanks,

Moh