Using ‘show call active voice brief’ to Track and Troubleshoot Voice Calls

Here is the information output that is sent every time the command is entered for

‘show call active voice brief’

Router#show call active voice brief

<ID>: <CallID> <start>ms.<index> +<connect> pid:<peer_id> <dir> <addr> <state>

dur hh:mm:ss tx:<packets>/<bytes> rx:<packets>/<bytes>

IP <ip>:<udp> rtt:<time>ms pl:<play>/<gap>ms lost:<lost>/<early>/<late>

delay:<last>/<min>/<max>ms <codec>

media inactive detected:<y/n> media cntrl rcvd:<y/n> timestamp:<time>

long duration call detected:<y/n> long duration call duration :<sec> timestamp:<time>

MODEMPASS <method> buf:<fills>/<drains> loss <overall%> <multipkt>/<corrected>

last <buf event time>s dur:<Min>/<Max>s

FR <protocol> [int dlci cid] vad:<y/n> dtmf:<y/n> seq:<y/n>

<codec> (payload size)

ATM <protocol> [int vpi/vci cid] vad:<y/n> dtmf:<y/n> seq:<y/n>

<codec> (payload size)

Tele <int> (callID) [channel_id] tx:<tot>/<v>/<fax>ms <codec> noise:<l> acom:<l> i/o:<l>/<l> dBm

MODEMRELAY info:<rcvd>/<sent>/<resent> xid:<rcvd>/<sent> total:<rcvd>/<sent>/<drops>

speeds(bps): local <rx>/<tx> remote <rx>/<tx>

Proxy <ip>:<audio udp>,<video udp>,<tcp0>,<tcp1>,<tcp2>,<tcp3> endpt: <type>/<manf>

bw: <req>/<act> codec: <audio>/<video>

tx: <audio pkts>/<audio bytes>,<video pkts>/<video bytes>,<t120 pkts>/<t120 bytes>

rx: <audio pkts>/<audio bytes>,<video pkts>/<video bytes>,<t120 pkts>/<t120 bytes>

This output is intended to clarify the output of the command, but there is some additional explanation that greatly helps in using this command.  This output can be used to parse the information that is shown, and can bring light to some of the specific fields would otherwise be fairly vague.  However, since this is the entire syntax of the command, and not every field is used in every call, there is quite a bit of extraneous data.

There are some important things shown in this command

- Packet loss and Jitter for calls

- Number of active calls

- Connected IP addresses

- UDP ports in use for calls

- Port and Interface for particular calls

- Dial peers matched for each leg

- Codec in use for a call

- Duration of current calls

Tracking a Call

Call ID: 	This 16 bit hex ID identifies the call, and typically there will be two legs for each active call.  Matching the two call legs will show where each leg is connected.

Controller:	This field exists in telephony legs, and identifies which Serial interface, controller, or voice port the call is active on.  This format of this will change based on the configuration of the controller.  Some examples:

T1 PRI: 0/0/1:23

E1 PRI: 0/0/1:15

T1 CAS: 0/0/1:0

FXO/FXS: 0/0/1

CME: 50/0/<ephone dn>

Channel:	For telephony legs this will show the particular channel of the PRI or CAS circuit in use, or the channel of the ephone-dn if it is a CME ephone.

Duration:	The duration of the call – this can be used to check against the time on the endpoints to track the call more accurately.

Dial Peer:	The pid: lists the dial peer matched for both legs of the call.

Calling Number:  	This will be listed for certain call flows where the gateway has the calling or called number information locally.  MGCP call flows, among others, will not list this for example.  This can be a very simple way to find a call.

IP Address:	For IP legs this can be used to identify an MTP in use, an IP phone, or another gateway.  By checking this address against an IP phone you can find where a particular call exists on a gateway.

- A good process for tracking the call is start with the duration, IP address, or calling/called number which is known, narrow the call down with the duration, and then match the Call ID to find which analog port and channel the call is using.

Troubleshooting Voice Quality

Channel: 	Some voice quality problems are related to specific controllers or specific channels on a circuit.  This field can be used to track whether voice quality is following a particular channel or interface.

Packet Loss/Jitter:  In this field, it is in the format of <lost packets/early packets/late packets>.  For troubleshooting purposes, both the early packets and late packets simply indicate jitter.   In this example, there is a packet loss of 15 packets.  This is enough to detect a problem, and a good call should not have any packet loss or jitter.  Jitter and packet less can cause static, pops, crackling, choppiness, and clipping of voice.

IP Address:	The IP address can be used to find where the RTP path is going, as well as track down which gateway or IP phone is in use.  For Cisco phones, there is a great deal of stream information that can be retrieved from the webpage of the phone.  If there is jitter or packet loss, this is the IP address that has the path with the problem.

Latency:	The minimum latency shown is seen in the example with 60/60/65ms.  According to ITU G.114 standards, the delay for a voice call should be less than 150 ms, but Cisco voice will perform better with a delay of less than 100 ms.  High latency can cause echo, static, and clipping of voice.

Codec:	This is an easy way to confirm which codec is in use.  If bandwidth is a factor, switching to a low bandwidth codec such as G.729 or G722 may improve voice quality.  Alternatively, G.711 will be able to handle packet loss more gracefully.

- If there are no lost or jittered packets, the delay is lower than 100-150ms, and the stream is directly to the phone, the quality is not caused in the IP network.

Troubleshooting One-way Audio

IP Address:	The IP address can be used to find where the RTP path is going, as well as track down which gateway or IP phone is in use.  For Cisco phones, there is a great deal of stream information that can be retrieved from the webpage of the phone.  The stream page of the phone will offer the IP address the phone is connected to, which is helpful in determining routing issues.  Confirm reachability from one address to the other.

Transmit / Receive

Counters: 	The transmit and receive counters are very helpful in determining if that leg is currently receiving or transmitting packets.  If the incoming call leg is not receiving packets, it will not transmit any out the outgoing call leg.  Troubleshooting one-way audio is simplified when it is determined whether the gateway is sending or receiving packets on a certain leg.  Having a rx: counter of zero typically means the far end does not have a route to the gateway.

- The webpage of the IP phone can also be used to check the default gateway as well as the stream statistics if it is sending and receiving packets.  Clicking the ‘?’ twice quickly while on a call with a Cisco IP phone will bring up a similar stream statistic menu.

Collecting a PCM Capture

A PCM capture is a procedure used by TAC to capture audio directly off of the DSPs for troubleshooting various audio issues, and should only be captured if required by TAC.

1. First, enable the capture buffer on the gateway:

Router(config)#voice hpi capture buffer 1000000

Next, check for free memory in the flash:

Router#dir flash:

Directory of flash:/

1  -rw-    45252276   Nov 3 2008 22:37:06 -05:00  c2800nm-ipvoice_ivs-mz.124-22.T

2  -rw-      496521  Aug 27 2008 21:36:30 -05:00  music-on-hold.au

63983616 bytes total (18231296 bytes free)

In this example there is approximately 18 MB free.  If there is not at least 15 MB or more of free flash, the PCM capture should be sent to a TFTP server.

2. Enable the destination for the capture

Router(config)#voice hpi capture destination flash:pcm.dat

or

Router(config)#voice hpi capture destination tftp://192.168.0.1/pcm.dat

It is important to understand that a PCM capture pulls the data directly from the audio stream, so the problem that you’re troubleshooting needs to be happening after the capture has started.

3.  Place the call, and keep the call up. Go to ‘Tracking a call’ and find the interface/controller for the call.  If this is a T1/E1, record the channel that the call is on as well.  The call can be found by combining the approximate call duration, the address of the IP phone (or other endpoint/gateway), or the calling/called numbers if available.  The Call ID will match an IP leg with a ‘Tele’ leg, and the controller and channel will be found in the Telephony leg.

3.  Once the call is up, and you have found the port and channel, you are ready to capture.  This command starts the PCM capture:

Router#test voice port <port.channel> pcm-dump caplog 7 duration 255

Note that if the circuit is on a channel, the <port.channel> will be similar to:  0/0/0:23.3

It will be the voice-port in use, followed by a period and the channel.

The command ‘show voice call stat’ will display the active calls in this format.

These are guidelines for the <port.channel> format:

T1 PRI:	0/0/0:23.channel

E1 PRI:	0/0/0:15.channel

T1 CAS:	0/0/0:0.channel

FXO/FXS: 	0/0/0

While the capture is running, reproduce the issue you’re troubleshooting.  To confirm that the PCM capture is running correctly, use ‘show voice hpi capture’.

If the capture is running correctly, you should see messages sent to URL:

Router#show voice hpi capture

HPI Capture is on and is logging to URL tftp://172.18.251.73/pcm.dat

5801 mesages sent to URL, 0 messages dropped

Message Buffer (total:inuse:free)  2049:0005:2044

Buffer Memory: 999912 bytes, Message size: 488 bytes

- Now the PCM capture is running, and you should try to reproduce the problem, or wait for up to a minute for the problem to happen.

- Disable the PCM capture:

Router#test voice port <port.channel> pcm-dump disable

- If the test was successful, remove the buffer and destination to prevent further writing to the file:

Router(config)#no voice hpi capture buffer 1000000

Router(config)#no voice hpi capture destination flash:pcm.dat

OR

Router(config)#no voice hpi capture buffer 1000000

Router(config)#no voice hpi capture destination tftp://192.168.0.1/pcm.dat

If the test was not successful, change the hpi destination:

Router(config)#voice hpi capture destination tftp://192.168.0.1/pcm2.dat

And delete the old file, and continue  at Step 3:

Router#delete flash:pcm.dat

7.  When completed, copy the pcm.dat flash to a tftp server (if it is on flash), and email to TAC.

# Text boxes

Note: The entry with Call ID of 2FFA, has duration of 4 seconds, is connected to 10.128.136.58 on port 8864, is a call between 5554039 and 5553236, and is on PRI 0/0/1:15 channel 25

Nick Matthews 01/05/2009