Current configuration : 3096 bytes

!

version 12.4

no service pad

service timestamps debug datetime msec

service timestamps log datetime msec

no service password-encryption

!

hostname Router

!

boot-start-marker

boot-end-marker

!

!

no aaa new-model

!

!

dot11 syslog

!

dot11 ssid BLAHBLAH

max-associations 10

authentication open

authentication key-management wpa

guest-mode

wpa-psk ascii 0 BLAHBLAH

!

ip cef

!

!

ip auth-proxy max-nodata-conns 3

ip admission max-nodata-conns 3

ip name-server x.x.x.x

ip name-server x.x.x.x

!

!

!

username root privilege 15 secret 5 BLAHBLAHBLAHBLAHBLAH

!

!

archive

log config

hidekeys

!

!

controller DSL 0

mode atm

line-term cpe

line-mode 2-wire line-zero

dsl-mode shdsl symmetric annex B

line-rate auto

!

!

bridge irb

!

!

interface BRI0

no ip address

encapsulation hdlc

shutdown

!

interface ATM0

no ip address

no atm ilmi-keepalive

!

interface ATM0.1 point-to-point

pvc 1/34

ubr 2048

encapsulation aal5mux ppp dialer

dialer pool-member 1

!

!

interface FastEthernet0

!

interface FastEthernet1

!

interface FastEthernet2

!

interface FastEthernet3

!

interface Dot11Radio0

no ip address

!

encryption mode ciphers tkip

!

ssid BLAHBLAH

!

speed basic-1.0 basic-2.0 basic-5.5 6.0 9.0 basic-11.0 18.0 24.0 36.0 48.0 54.0

channel 2412

station-role root

world-mode dot11d country AU indoor

bridge-group 1

bridge-group 1 subscriber-loop-control

bridge-group 1 spanning-disabled

bridge-group 1 block-unknown-source

no bridge-group 1 source-learning

no bridge-group 1 unicast-flooding

!

interface Vlan1

no ip address

bridge-group 1

!

interface Dialer0

ip address negotiated

ip flow ingress

ip nat outside

ip virtual-reassembly

encapsulation ppp

dialer pool 1

dialer-group 1

no cdp enable

ppp authentication chap callin

ppp chap hostname BLAHBLAH

ppp chap password 0 BLAH

!

interface BVI1

ip address 10.0.29.254 255.255.255.0

no ip redirects

ip local-proxy-arp

ip flow ingress

ip flow egress

ip nat inside

ip virtual-reassembly

ip route-cache same-interface

!

ip forward-protocol nd

ip route 0.0.0.0 0.0.0.0 Dialer0

!

no ip http server

no ip http secure-server

ip nat inside source list 101 interface Dialer0 overload

ip nat inside source static tcp 10.0.29.10 25 interface Dialer0 25

!

ip access-list extended TerminalAccess

permit ip 10.0.29.0 0.0.0.255 any

permit tcp x.x.x.x 0.0.0.255 any eq 22

permit udp x.x.x.x 0.0.0.255 any eq snmp

deny   tcp any any log

!

access-list 22 permit 10.0.29.0 0.0.0.255

access-list 101 permit ip 10.0.0.0 0.255.255.255 any

!

!

!

control-plane

!

bridge 1 protocol ieee

bridge 1 route ip

!

line con 0

no modem enable

line aux 0

line vty 0 4

access-class TerminalAccess in

privilege level 15

login local

transport input telnet ssh

!

scheduler max-task-time 5000

ntp clock-period 17175144

ntp server x.x.x.x

end