| Cisco Site |  |
| --- | --- |
| IP sec tunnel endpoint: LAN Subnet: | 1.1.1.1.1 192.168.100.0/24 |
| Juniper Site |  |
| IP sec tunnel endpoint: LAN Subnet: | 2.2.2.2 192.168.200.0/24 |
| Phase 1 - IKE Policy Definition (ISAKMP) |  |
| IKE Mode Message Encryption Algorithm: Message Integrity (Hash) Algorith: Peer authentigateon method: Peer authentication key: Key exchange DH group identifier: ISAKMP policy Lifetime (sec): | Main 3des-cbc ah-sha-hmac pre-shared <Testkey> 2 (1024 bits) 28800 (8 hour(s)) |
| Phase 2 - IKE Policy Definition (IPSEC) |  |
| IPSec Mode: IPSec SA Lifetime (sec): Perfect Forward Secrecy (PFS) IKE Mode Mechanism for Payload Authentication(ESP): Mechanism for Payload Encryption (ESP): Encryption IPSEC Packet Fragmentation | Tunnel 3600 (1 hour(s)) 2 (1024 bits)) quick esp-sha-hmac esp-3des-cbc none Pre-Fragmentation |

Juniper Configuration

interfaces {

fe-0/0/0 {

speed 10m;

link-mode half-duplex;

unit 0 {

family inet {

address 1.1.1.1/24;

}

}

}

fe-0/0/1 {

speed 100m;

unit 0 {

family inet {

address 192.168.100.1/24;

}

}

}

sp-0/0/0 {

traceoptions {

flag all;

}

services-options {

syslog {

host local {

services info;

}

}

}

unit 0 {

family inet;

}

unit 1 {

family inet;

service-domain inside;

}

unit 2 {

family inet;

service-domain outside;

}

}

lo0 {

unit 0 {

family inet {

address 127.0.0.1/32;

}

}

}

}

snmp {

community public;

}

routing-options {

route 2.2.2.2/32 next-hop 1.1.1.254;

route 192.168.200.0/24 next-hop sp-0/0/0.1;

}

}

services {

service-set ipsec-service {

next-hop-service {

inside-service-interface sp-0/0/0.1;

outside-service-interface sp-0/0/0.2;

}

ipsec-vpn-options {

local-gateway 1.1.1.1;

}

ipsec-vpn-rules ike-rule;

}

ipsec-vpn {

rule ike-rule {

term term-ike {

from {

source-address {

192.168.100.0/24;

}

destination-address {

192.168.200.0/24;

}

}

then {

remote-gateway 2.2.2.2;

dynamic {

ike-policy ike-preshare;

ipsec-policy phase2;

}

}

}

match-direction input;

}

ipsec {

proposal ph2-3des-sha-esp {

protocol esp;

authentication-algorithm hmac-sha1-96;

encryption-algorithm 3des-cbc;

}

policy phase2 {

perfect-forward-secrecy {

keys group2;

}

proposals ph2-3des-sha-esp;

}

}

ike {

proposal ike-3des-sha-dh2 {

dh-group group2;

authentication-algorithm sha1;

encryption-algorithm 3des-cbc;

}

policy ike-preshare {

proposals ike-3des-sha-dh2;

pre-shared-key ascii-text <testkey>;

}

}

establish-tunnels immediately;

}

}

Cisco Configuration

!

crypto isakmp enable

!

crypto isakmp policy 10

encr 3des

hash sha

authentication pre-share

group 2

lifetime 28800

!

crypto isakmp identity address

crypto isakmp key testkey  address 1.1.1.1

!

interface Ethernet0

description Connection Private Network

ip address 192.168.200.1 255.255.255.0

!

interface Ethernet1

description Connection Public Network

ip address 2.2.2.2 255.255.255.250

crypto map VPN

!

crypto ipsec transform-set espSHA3DES esp-3des esp-sha-hmac

!

!

access-list 105 permit ip 192.168.200.0 0.0.0.255 192.168.100.0 0.0.0.255

!

crypto map VPN 5 ipsec-isakmp

set peer 1.1.1.1

set security-association lifetime seconds 3600

set pfs group2

set transform-set espSHA3DES

match address 105

!

!

ip route 0.0.0.0 0.0.0.0 2.2.2.254

!