What can you determine from this:

Three random locations, in different states!  I have recently taken over these divisions and noticed that unlike the rest they are using a NTP SERVER of 199.250.138.1 which appears to be a ISP of some sort!  Now the previous admin, is no longer around form me to consult! No one is suppose to have console accesss and we use TACAS for our Net. admins to access!  None of them have done anything to these devices! My local Telco has opened proactive tickets on these locations, because these devices appear to go off line!  They obviously are not going off line, if

1. someone is console into them and the log is recorded

2. they are administrativly shuting down FA interface, and etc.

Here is the SYS LOGS from the three devices:

I.Syslog logging: enabled (1 messages dropped, 2 messages rate-limited,

0 flushes, 0 overruns, xml disabled, filtering disabled)

Console logging: disabled

Monitor logging: disabled

Buffer logging: level debugging, 29 messages logged, xml disabled,

filtering disabled

Logging Exception size (4096 bytes)

Count and timestamp logging messages: disabled

No active filter modules.

Trap logging: level errors, 3 message lines logged

Logging to 10.110.23.155 (udp port 514, audit disabled, link up), 3 message lines logged, xml disabled,

filtering disabled

Log Buffer (4096 bytes):

*Jul 22 16:22:19.127: SERVICE_MODULE(Serial0/1/0): self test finished: Passedsslinit fn

*Jul 22 16:22:23.655: %VPN_HW-6-INFO_LOC: Crypto engine: onboard 0  State changed to: Initialized

*Jul 22 16:22:23.659: %VPN_HW-6-INFO_LOC: Crypto engine: onboard 0  State changed to: Enabled

*Jul 22 16:22:24.143: %LINK-3-UPDOWN: Interface Serial0/1/0, changed state to down

*Jul 22 16:22:25.143: %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/1/0, changed state to down

*Jul 22 16:22:26: %SYS-6-CLOCKUPDATE: System clock has been updated from 16:22:26 UTC Sun Jul 22 2007 to 11:22:26 EST Sun Jul 22 2007, configured from console by console.

*Jul 22 16:22:26: %SYS-6-CLOCKUPDATE: System clock has been updated from 11:22:26 EST Sun Jul 22 2007 to 12:22:26 EDT Sun Jul 22 2007, configured from console by console.

*Jul 22 16:22:27: %LINK-5-CHANGED: Interface FastEthernet0/1, changed state to administratively down

*Jul 22 16:22:27: %SYS-5-CONFIG_I: Configured from memory by console

*Jul 22 16:22:27: %LINEPROTO-5-UPDOWN: Line protocol on Interface Loopback0, changed state to up

*Jul 22 16:22:27: %SYS-5-RESTART: System restarted --

Cisco IOS Software, 2801 Software (C2801-ADVSECURITYK9-M), Version 12.4(3e), RELEASE SOFTWARE (fc2)

Technical Support: http://www.cisco.com/techsupport

Copyright (c) 1986-2006 by Cisco Systems, Inc.

Compiled Wed 14-Jun-06 01:33 by alnguyen

*Jul 22 16:22:28: %SNMP-5-COLDSTART: SNMP agent on host Orange_Park_FL is undergoing a cold start

*Jul 22 16:22:28: %SSH-5-ENABLED: SSH 1.99 has been enabled

*Jul 22 16:22:28: %CRYPTO-6-ISAKMP_ON_OFF: ISAKMP is OFF

*Jul 22 16:22:28: %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/1, changed state to down

*Jul 22 16:22:28: %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up

*Jul 22 16:22:29: %SYS-6-LOGGINGHOST_STARTSTOP: Logging to host 10.110.23.155 started - CLI initiated

*Jul 22 16:22:30: %LINK-3-UPDOWN: Interface FastEthernet0/0, changed state to up

*Jul 22 16:22:33: %LINK-3-UPDOWN: Interface Serial0/1/0, changed state to up

*Jul 22 16:22:44: %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/1/0, changed state to up

*Jul 22 16:23:24: %DUAL-5-NBRCHANGE: IP-EIGRP(0) 100: Neighbor 10.1.5.57 (Serial0/1/0.122) is up: new adjacency

*Jul 24 05:42:50: %DUAL-5-NBRCHANGE: IP-EIGRP(0) 100: Neighbor 10.1.5.57 (Serial0/1/0.122) is down: Interface Goodbye received

*Jul 24 05:42:55: %DUAL-5-NBRCHANGE: IP-EIGRP(0) 100: Neighbor 10.1.5.57 (Serial0/1/0.122) is up: new adjacency

*Jul 24 05:43:06: %DUAL-5-NBRCHANGE: IP-EIGRP(0) 100: Neighbor 10.1.5.57 (Serial0/1/0.122) is down: interface down

*Jul 24 05:43:07: %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/1/0, changed state to down

*Jul 24 05:44:17: %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/1/0, changed state to up

*Jul 24 05:44:56: %DUAL-5-NBRCHANGE: IP-EIGRP(0) 100: Neighbor 10.1.5.57 (Serial0/1/0.122) is up: new adjacency

II. Syslog logging: enabled (1 messages dropped, 2 messages rate-limited,

0 flushes, 0 overruns, xml disabled, filtering disabled)

Console logging: disabled

Monitor logging: disabled

Buffer logging: level debugging, 24 messages logged, xml disabled,

filtering disabled

Logging Exception size (4096 bytes)

Count and timestamp logging messages: disabled

No active filter modules.

Trap logging: level errors, 3 message lines logged

Logging to 10.110.23.155 (udp port 514, audit disabled, link up), 3 message lines logged, xml disabled,

filtering disabled

Log Buffer (4096 bytes):

*Jul 14 15:41:56.127: SERVICE_MODULE(Serial0/1/0): self test finished: Passedsslinit fn

*Jul 14 15:42:00.651: %VPN_HW-6-INFO_LOC: Crypto engine: onboard 0  State changed to: Initialized

*Jul 14 15:42:00.655: %VPN_HW-6-INFO_LOC: Crypto engine: onboard 0  State changed to: Enabled

*Jul 14 15:42:01.139: %LINK-3-UPDOWN: Interface Serial0/1/0, changed state to down

*Jul 14 15:42:02.139: %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/1/0, changed state to down

*Jul 14 15:42:03: %SYS-6-CLOCKUPDATE: System clock has been updated from 15:42:03 UTC Sat Jul 14 2007 to 10:42:03 EST Sat Jul 14 2007, configured from console by console.

*Jul 14 15:42:03: %SYS-6-CLOCKUPDATE: System clock has been updated from 10:42:03 EST Sat Jul 14 2007 to 11:42:03 EDT Sat Jul 14 2007, configured from console by console.

*Jul 14 15:42:04: %LINK-5-CHANGED: Interface FastEthernet0/1, changed state to administratively down

*Jul 14 15:42:04: %SYS-5-CONFIG_I: Configured from memory by console

*Jul 14 15:42:04: %LINEPROTO-5-UPDOWN: Line protocol on Interface Loopback0, changed state to up

*Jul 14 15:42:05: %SYS-5-RESTART: System restarted --

Cisco IOS Software, 2801 Software (C2801-ADVSECURITYK9-M), Version 12.4(3e), RELEASE SOFTWARE (fc2)

Technical Support: http://www.cisco.com/techsupport

Copyright (c) 1986-2006 by Cisco Systems, Inc.

Compiled Wed 14-Jun-06 01:33 by alnguyen

*Jul 14 15:42:05: %SNMP-5-COLDSTART: SNMP agent on host Rego_Park is undergoing a cold start

*Jul 14 15:42:05: %SSH-5-ENABLED: SSH 1.99 has been enabled

*Jul 14 15:42:05: %CRYPTO-6-ISAKMP_ON_OFF: ISAKMP is OFF

*Jul 14 15:42:05: %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/1, changed state to down

*Jul 14 15:42:05: %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to down

*Jul 14 15:42:06: %SYS-6-LOGGINGHOST_STARTSTOP: Logging to host 10.110.23.155 started - CLI initiated

*Jul 14 15:42:12: %LINK-3-UPDOWN: Interface Serial0/1/0, changed state to up

*Jul 14 15:42:14: %LINK-3-UPDOWN: Interface FastEthernet0/0, changed state to up

*Jul 14 15:42:15: %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up

*Jul 14 15:42:23: %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/1/0, changed state to up

*Jul 14 15:43:05: %DUAL-5-NBRCHANGE: IP-EIGRP(0) 100: Neighbor 10.1.4.121 (Serial0/1/0.168) is up: new adjacency

III. Syslog logging: enabled (1 messages dropped, 2 messages rate-limited,

0 flushes, 0 overruns, xml disabled, filtering disabled)

Console logging: level debugging, 23 messages logged, xml disabled,

filtering disabled

Monitor logging: level debugging, 0 messages logged, xml disabled,

filtering disabled

Buffer logging: level debugging, 23 messages logged, xml disabled,

filtering disabled

Logging Exception size (4096 bytes)

Count and timestamp logging messages: disabled

No active filter modules.

Trap logging: level informational, 24 message lines logged

Logging to 199.250.138.104 (udp port 514, audit disabled, link up), 24 message lines logged, xml disabled,

filtering disabled

Log Buffer (4096 bytes):

*Jul 14 07:36:28.119: SERVICE_MODULE(Serial0/1/0): self test finished: Passedsslinit fn

*Jul 14 07:36:31.759: %VPN_HW-6-INFO_LOC: Crypto engine: onboard 0  State changed to: Initialized

*Jul 14 07:36:31.763: %VPN_HW-6-INFO_LOC: Crypto engine: onboard 0  State changed to: Enabled

*Jul 14 07:36:32.247: %LINK-3-UPDOWN: Interface Serial0/1/0, changed state to down

*Jul 14 07:36:33.247: %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/1/0, changed state to down

*Jul 14 02:36:34.163: %SYS-6-CLOCKUPDATE: System clock has been updated from 07:36:34 UTC Sat Jul 14 2007 to 02:36:34 EST Sat Jul 14 2007, configured from console by console.

*Jul 14 03:36:34.163: %SYS-6-CLOCKUPDATE: System clock has been updated from 02:36:34 EST Sat Jul 14 2007 to 03:36:34 EDT Sat Jul 14 2007, configured from console by console.

*Jul 14 03:36:34.427: %LINK-5-CHANGED: Interface FastEthernet0/1, changed state to administratively down

*Jul 14 03:36:34.792: %SYS-5-CONFIG_I: Configured from memory by console

*Jul 14 03:36:35.008: %LINK-3-UPDOWN: Interface FastEthernet0/0, changed state to up

*Jul 14 03:36:35.397: %LINEPROTO-5-UPDOWN: Line protocol on Interface Loopback0, changed state to up

*Jul 14 03:36:35.521: %SYS-5-RESTART: System restarted --

Cisco IOS Software, 2801 Software (C2801-ADVSECURITYK9-M), Version 12.4(3d), RELEASE SOFTWARE (fc3)

Technical Support: http://www.cisco.com/techsupport

Copyright (c) 1986-2006 by Cisco Systems, Inc.

Compiled Wed 19-Apr-06 11:56 by alnguyen

*Jul 14 03:36:35.525: %SNMP-5-COLDSTART: SNMP agent on host Waco_TX is undergoing a cold start

*Jul 14 03:36:35.541: %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/1, changed state to down

*Jul 14 03:36:35.841: %CRYPTO-6-ISAKMP_ON_OFF: ISAKMP is OFF

*Jul 14 03:36:35.953: %SYS-6-LOGGINGHOST_STARTSTOP: Logging to host 199.250.138.104 started - CLI initiated

*Jul 14 03:36:36.010: %LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up

*Jul 14 03:36:38.237: %LINK-3-UPDOWN: Interface FastEthernet0/0, changed state to up

*Jul 14 03:36:47.685: %LINK-3-UPDOWN: Interface Serial0/1/0, changed state to up

*Jul 14 03:36:58.703: %LINEPROTO-5-UPDOWN: Line protocol on Interface Serial0/1/0, changed state to up

*Jul 14 03:37:40.404: %DUAL-5-NBRCHANGE: IP-EIGRP(0) 100: Neighbor 10.1.3.177 (Serial0/1/0.600) is up: new adjacency

Please Advise!