| KMC# interface FastEthernet0/1 description Allocated subnet from VISI ip address 208.42.157.253 255.255.255.0 interface Hssi1/0 description Link to KMC ip address 64.238.244.130 255.255.255.252 ! router bgp 29896 no synchronization no bgp log-neighbor-changes network 64.238.244.128 mask 255.255.255.252 network 208.42.157.0 neighbor 64.238.244.129 remote-as 23126 neighbor 64.238.244.129 description KMC Telecom neighbor 64.238.244.129 soft-reconfiguration inbound neighbor 64.238.244.129 password 7 100D025F0654 neighbor 64.238.244.129 filter-list 85 in neighbor 64.238.244.129 filter-list 80 out neighbor 208.42.157.248 remote-as 29896 neighbor 208.42.157.248 next-hop-self neighbor 208.42.157.248 filter-list 90 out neighbor 208.42.157.249 remote-as 29896 neighbor 208.42.157.249 next-hop-self neighbor 208.42.157.249 filter-list 90 out neighbor 208.42.157.254 remote-as 29896 neighbor 208.42.157.254 next-hop-self neighbor 208.42.157.254 version 4 no auto-summary ! ip as-path access-list 80 permit ^$ ip as-path access-list 85 permit ^23126_[0-9]*$ ip as-path access-list 90 permit ^$ ip as-path access-list 90 permit ^23126$ KMC# sh ip route Gateway of last resort is 64.238.244.129 to network 0.0.0.0 64.0.0.0/30 is subnetted, 1 subnets C 64.238.244.128 is directly connected, Hssi1/0 C 208.42.157.0/24 is directly connected, FastEthernet0/1 208.42.22.0/30 is subnetted, 1 subnets B 208.42.22.196 [200/0] via 208.42.157.254, 1w6d B* 0.0.0.0/0 [20/0] via 64.238.244.129, 7w0d | C_7200# interface FastEthernet0/1 description Multihome assigned subnet ip address 208.42.157.254 255.255.255.0 ! interface Hssi1/0 ip address 208.42.22.198 255.255.255.252 router bgp 29896 no synchronization bgp log-neighbor-changes network 208.42.22.196 mask 255.255.255.252 network 208.42.71.64 mask 255.255.255.240 network 208.42.157.0 neighbor 208.42.22.197 remote-as 8015 neighbor 208.42.22.197 description VISI DS-3 neighbor 208.42.22.197 soft-reconfiguration inbound neighbor 208.42.22.197 password 7 03546D4A432671 neighbor 208.42.22.197 filter-list 85 in neighbor 208.42.22.197 filter-list 80 out neighbor 208.42.157.248 remote-as 29896 neighbor 208.42.157.248 next-hop-self neighbor 208.42.157.248 filter-list 90 out neighbor 208.42.157.249 remote-as 29896 neighbor 208.42.157.249 next-hop-self neighbor 208.42.157.249 filter-list 90 out neighbor 208.42.157.253 remote-as 29896 neighbor 208.42.157.253 version 4 no auto-summary ip as-path access-list 80 permit ^$ ip as-path access-list 85 permit ^8015_[0-9]*$ ip as-path access-list 90 permit ^8015$ route-map TUNNEL_ADDRS permit 10 match ip address 98 set community no-advertise C_7200#sh ip route Gateway of last resort is 208.42.22.197 to network 0.0.0.0 64.0.0.0/30 is subnetted, 1 subnets B 64.238.244.128 [200/0] via 208.42.157.253, 7w0d C 208.42.157.0/24 is directly connected, FastEthernet0/1 208.42.22.0/30 is subnetted, 1 subnets C 208.42.22.196 is directly connected, Hssi1/0 B* 0.0.0.0/0 [20/0] via 208.42.22.197, 1w6d |
| --- | --- |