SW1:

VLAN0001

Spanning tree enabled protocol ieee

Root ID Priority    32769

Address     0015.c663.4f00

This bridge is the root

Hello Time   2 sec  Max Age 20 sec  Forward Delay 15 sec

Bridge ID  Priority    32769  (priority 32768 sys-id-ext 1)

Address     0015.c663.4f00

Hello Time   2 sec  Max Age 20 sec  Forward Delay 15 sec

Aging Time 300

Interface        Role Sts Cost      Prio.Nbr Type

---------------- ---- --- --------- -------- --------------------------------

Gi0/1            Desg FWD 4         128.1    P2p

Gi0/4            Desg FWD 4         128.28   P2p

VLAN0051

Spanning tree enabled protocol ieee

Root ID Priority    32819

Address     0015.c663.4f00

This bridge is the root

Hello Time   2 sec  Max Age 20 sec  Forward Delay 15 sec

Bridge ID  Priority    32819  (priority 32768 sys-id-ext 51)

Address     0015.c663.4f00

Hello Time   2 sec  Max Age 20 sec  Forward Delay 15 sec

Aging Time 300

Interface        Role Sts Cost      Prio.Nbr Type

---------------- ---- --- --------- -------- --------------------------------

Gi0/1            Desg FWD 4         128.1    P2p

Gi0/4            Desg FWD 4         128.28   P2p

VLAN0054

Spanning tree enabled protocol ieee

Root ID    Priority    32822

Address     0015.c663.4f00

This bridge is the root

Hello Time   2 sec  Max Age 20 sec  Forward Delay 15 sec

Bridge ID  Priority    32822  (priority 32768 sys-id-ext 54)

Address     0015.c663.4f00

Hello Time   2 sec  Max Age 20 sec  Forward Delay 15 sec

Aging Time 300

Interface        Role Sts Cost      Prio.Nbr Type

---------------- ---- --- --------- -------- --------------------------------

Gi0/1            Desg FWD 4         128.1    P2p

Gi0/4            Desg FWD 4         128.28   P2p

VLAN0056

Spanning tree enabled protocol ieee

Root ID    Priority    32824

Address     0015.c663.4f00

This bridge is the root

Hello Time   2 sec  Max Age 20 sec  Forward Delay 15 sec

Bridge ID  Priority    32824  (priority 32768 sys-id-ext 56)

Address     0015.c663.4f00

Hello Time   2 sec  Max Age 20 sec  Forward Delay 15 sec

Aging Time 300

Interface        Role Sts Cost      Prio.Nbr Type

---------------- ---- --- --------- -------- --------------------------------

Gi0/1            Desg FWD 4         128.1    P2p

Gi0/4            Desg FWD 4         128.28   P2p