36#sh run

Building configuration...

Current configuration : 1411 bytes

!

version 12.2

service timestamps debug datetime msec

service timestamps log datetime msec

no service password-encryption

!

hostname 36

!

logging queue-limit 100

no logging console

enable secret 5 $1$RYDB$us.a.xb57tswn.UMFV1Tt/

!

ip subnet-zero

!

!

!

ip audit notify log

ip audit po max-events 100

!

!

!

!

!

!

!

!

!

!

!

!

no voice hpi capture buffer

no voice hpi capture destination

!

!

mta receive maximum-recipients 0

!

!

!

!

interface Loopback0

ip address 192.168.168.65 255.255.255.192

!

interface FastEthernet0/0

ip address 10.10.10.2 255.255.255.0

duplex auto

speed 10

!

interface Serial0/0

no ip address

!

interface FastEthernet0/1

ip address 10.1.1.3 255.255.255.0

duplex auto

speed 10

!

interface Serial0/1

ip address 172.20.1.1 255.255.255.252

!

router ospf 123

log-adjacency-changes

redistribute bgp 10 subnets

network 10.1.1.0 0.0.0.255 area 0

!

router bgp 10

no synchronization

bgp log-neighbor-changes

network 172.20.1.0 mask 255.255.255.252

network 192.168.168.64 mask 255.255.255.192

redistribute ospf 123 metric 100

neighbor 10.10.10.1 remote-as 10

neighbor 10.10.10.1 next-hop-self

neighbor 172.20.1.2 remote-as 30

no auto-summary

!

no ip http server

no ip http secure-server

ip classless

!

ip as-path access-list 1 permit ^$

!

!

!

call rsvp-sync

!

!

mgcp profile default

!

dial-peer cor custom

!

!

!

!

!

line con 0

line aux 0

line vty 0 4

password abc

login

!

!

end

36#sh ip ro

Codes: C - connected, S - static, R - RIP, M - mobile, B - BGP

D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area

N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2

E1 - OSPF external type 1, E2 - OSPF external type 2

i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area

* - candidate default, U - per-user static route, o - ODR

P - periodic downloaded static route

Gateway of last resort is not set

202.122.64.0/26 is subnetted, 4 subnets

O       202.122.64.192 [110/20] via 10.1.1.1, 00:19:02, FastEthernet0/1

O       202.122.64.128 [110/20] via 10.1.1.1, 00:19:02, FastEthernet0/1

O       202.122.64.64 [110/11] via 10.1.1.1, 00:19:02, FastEthernet0/1

O       202.122.64.0 [110/11] via 10.1.1.1, 00:19:02, FastEthernet0/1

202.122.65.0/26 is subnetted, 4 subnets

B       202.122.65.192 [20/0] via 172.20.1.2, 00:17:23

B       202.122.65.128 [20/0] via 172.20.1.2, 00:17:23

B       202.122.65.64 [20/0] via 172.20.1.2, 00:17:23

B       202.122.65.0 [20/0] via 172.20.1.2, 00:17:23

172.20.0.0/30 is subnetted, 2 subnets

C       172.20.1.0 is directly connected, Serial0/1

B       172.20.1.4 [20/0] via 172.20.1.2, 00:17:23

10.0.0.0/24 is subnetted, 3 subnets

B       10.1.2.0 [20/0] via 172.20.1.2, 00:17:23

C       10.10.10.0 is directly connected, FastEthernet0/0

C       10.1.1.0 is directly connected, FastEthernet0/1

192.168.170.0/26 is subnetted, 4 subnets

B       192.168.170.192 [20/0] via 172.20.1.2, 00:17:23

B       192.168.170.128 [20/0] via 172.20.1.2, 00:17:23

B       192.168.170.64 [20/0] via 172.20.1.2, 00:17:23

B       192.168.170.0 [20/0] via 172.20.1.2, 00:17:23

192.168.1.0/30 is subnetted, 2 subnets

O E2    192.168.1.0 [110/1] via 10.1.1.2, 00:07:56, FastEthernet0/1

O E2    192.168.1.4 [110/1] via 10.1.1.2, 00:07:47, FastEthernet0/1

192.168.168.0/26 is subnetted, 2 subnets

C       192.168.168.64 is directly connected, Loopback0

O E2    192.168.168.0 [110/1] via 10.1.1.2, 00:18:57, FastEthernet0/1

192.168.169.0/26 is subnetted, 4 subnets

O E2    192.168.169.192 [110/1] via 10.1.1.2, 00:07:47, FastEthernet0/1

O E2    192.168.169.128 [110/1] via 10.1.1.2, 00:07:47, FastEthernet0/1

O E2    192.168.169.64 [110/1] via 10.1.1.2, 00:07:47, FastEthernet0/1

O E2    192.168.169.0 [110/1] via 10.1.1.2, 00:07:47, FastEthernet0/1

36# sh ip bgp

BGP table version is 74, local router ID is 192.168.168.65

Status codes: s suppressed, d damped, h history, * valid, > best, i - internal,

r RIB-failure, S Stale

Origin codes: i - IGP, e - EGP, ? - incomplete

Network          Next Hop            Metric LocPrf Weight Path

*> 10.1.1.0/24      0.0.0.0                  0         32768 ?

* i                 10.10.10.1               0    100      0 ?

* i10.1.2.0/24      10.10.10.1               0    100      0 20 40 i

*>                  172.20.1.2                             0 30 50 i

*> 172.20.1.0/30    0.0.0.0                  0         32768 i

*                   172.20.1.2               0             0 30 i

*> 172.20.1.4/30    172.20.1.2               0             0 30 i

r>i192.168.1.0/30   10.10.10.1               0    100      0 i

r>i192.168.1.4/30   10.10.10.1               0    100      0 20 i

r>i192.168.168.0/26 10.10.10.1               0    100      0 i

*> 192.168.168.64/26

0.0.0.0                  0         32768 i

r>i192.168.169.0/26 10.10.10.1               0    100      0 20 i

r>i192.168.169.64/26

10.10.10.1               0    100      0 20 i

r>i192.168.169.128/26

10.10.10.1               0    100      0 20 40 i

Network          Next Hop            Metric LocPrf Weight Path

r                   172.20.1.2                             0 30 50 60 40 i

r>i192.168.169.192/26

10.10.10.1               0    100      0 20 40 i

r                   172.20.1.2                             0 30 50 60 40 i

*> 192.168.170.0/26 172.20.1.2               0             0 30 i

*> 192.168.170.64/26

172.20.1.2               0             0 30 i

*> 192.168.170.128/26

172.20.1.2                             0 30 50 i

*> 192.168.170.192/26

172.20.1.2                             0 30 50 i

*> 202.122.64.0/26  10.1.1.1               100         32768 ?

* i                 10.10.10.1             100    100      0 ?

*> 202.122.64.64/26 10.1.1.1               100         32768 ?

* i                 10.10.10.1             100    100      0 ?

*> 202.122.64.128/26

10.1.1.1               100         32768 ?

* i                 10.10.10.1             100    100      0 ?

*> 202.122.64.192/26

10.1.1.1               100         32768 ?

* i                 10.10.10.1             100    100      0 ?

* i202.122.65.0/26  10.10.10.1               0    100      0 20 40 60 i

Network          Next Hop            Metric LocPrf Weight Path

*>                  172.20.1.2                             0 30 50 60 i

* i202.122.65.64/26 10.10.10.1               0    100      0 20 40 60 i

*>                  172.20.1.2                             0 30 50 60 i

* i202.122.65.128/26

10.10.10.1               0    100      0 20 40 60 i

*>                  172.20.1.2                             0 30 50 60 i

* i202.122.65.192/26

10.10.10.1               0    100      0 20 40 60 i

*>                  172.20.1.2                             0 30 50 60 i