Mumbai – Pune Tunnel Config

| Mumbai Router 10.0.0.1 | Pune Router 200.2.5.6 |
| --- | --- |
| Interface Fa 0/0/1 Ip add 10.0.0.1 255.255.255.0 Des “Local” Interface Fa 0/0/0 Ip add 10.5.2.2 255.255.255.252 Des “ Connected To VSNL POP “ Interface Fa 0/0/3 Ip add 10.5.1.9 255.255.255.252 Des “ Connected To REL POP “ Inter tunnel 0 vsnl Ip add 10.10.1.1 255.255.255.252 Tunnel source 10.5.2.2 Tunnel destination 10.5.2.90 Keepalive 3 2 Inter tunnel 1 Rel Ip add 10.10.2.1 255.255.255.252 Tunnel source 10.5.1.9 Tunnel destination 10.5.1.21 Keepalive 3 2 | Interface Fa 0/0 Ip add 200.2.5.6 255.255.255.0 Des “Local” Interface Fa 0/1 Ip add 10.5.2.90 255.255.255.252 Des “ Connected To VSNL POP “ Interface serial 0/3/0 Ip add 10.5.1.21 255.255.255.252 Des “ Connected To REL POP “ Inter tunnel 0 vsnl Ip add 10.10.1.2 255.255.255.252 Tunnel source 10.5.2.90 Tunnel destination 10.5.2.2 Keepalive 3 2 Inter tunnel 1 Rel Ip add 10.10.2.2 255.255.255.252 Tunnel source 10.5.1.21 Tunnel destination 10.5.1.9 Keepalive 3 2 |

Static Routing Backup Using Object Tracking

On Mumbai Router

Mumbai# configure terminal

Mumbai (config)# ip sla monitor 1

Mumbai (config-sla-monitor)# type echo protocol ipIcmpEcho 10.5.1.21 source-ipaddr 10.5.1.9

Mumbai (config-sla-monitor-echo)# timeout 1000           msec

Mumbai (config-sla-monitor-echo)# frequency 3             sec

Mumbai (config-sla-monitor-echo)# threshold 2              msec

Mumbai (config-sla-monitor-echo)# exit

Mumbai (config)# ip sla monitor schedule 1 life forever start-time now

Mumbai (config)# track 123 rtr 1 reachability

Mumbai (config)# ip route 200.2.5.0 255.255.255.0 10.5.1.10   (Primary)

Mumbai (config)# ip route 200.2.5.0 255.255.255.0 10.5.2.1 100  (Secondary with metric)

On Pune Router

Pune # configure terminal

Pune (config)# ip sla monitor 1

Pune (config-sla-monitor)# type echo protocol ipIcmpEcho 10.5.1.9 source-ipaddr 10.5.1.21

Pune (config-sla-monitor-echo)# timeout 1000           msec

Pune (config-sla-monitor-echo)# frequency 3             sec

Pune (config-sla-monitor-echo)# threshold 2              msec

Pune (config-sla-monitor-echo)# exit

Pune (config)# ip sla monitor schedule 1 life forever start-time now

Pune (config)# track 123 rtr 1 reachability

ip route 10.0.0.0 255.255.0.0 10.5.1.22

ip route 10.0.0.0 255.255.0.0 10.5.2.89 100