!

version 12.2

service timestamps debug uptime

service timestamps log uptime

no service password-encryption

!

hostname B1-F0-CORE1

!

boot system flash s72033-pk9sv-mz.122-17d.SXB9.bin

logging snmp-authfail

aaa new-model

enable secret 5 $1$arQN$TUAOEHwvDpPvqFogGR9oD.

enable password cisco

!

firewall multiple-vlan-interfaces

firewall module 7 vlan-group 1

firewall module 8 vlan-group 1

firewall vlan-group 1  10,30,40,50,60,80,100,110,120,130,800,900

intrusion-detection module 9 management-port access-vlan 30

udld enable

ip subnet-zero

!

!

ip domain-name Someone

ip name-server 192.168.10.10

ip name-server 192.168.10.11

!

mpls ldp logging neighbor-changes

mls rp ip

mls flow ip interface-full

no mls flow ipv6

mls sampling time-based 64

mls cef error action freeze

!

!

!

!

!

!

spanning-tree mode pvst

spanning-tree loopguard default

no spanning-tree optimize bpdu transmission

hw-module slot 6 memory test full

diagnostic cns publish cisco.cns.device.diag_results

diagnostic cns subscribe cisco.cns.dev

!

redundancy

mode sso

main-cpu

auto-sync running-config

auto-sync standard

!

vlan internal allocation policy ascending

vlan access-log ratelimit 2000

!

!

interface GigabitEthernet1/1

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/2

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/3

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/4

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

spanning-tree portfast

!

interface GigabitEthernet1/5

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

spanning-tree portfast

!

interface GigabitEthernet1/6

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

spanning-tree portfast

!

interface GigabitEthernet1/7

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

spanning-tree portfast

!

interface GigabitEthernet1/8

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

spanning-tree portfast

!

interface GigabitEthernet1/9

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

spanning-tree portfast

!

interface GigabitEthernet1/10

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

spanning-tree portfast

!

interface GigabitEthernet1/11

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

spanning-tree portfast

!

interface GigabitEthernet1/12

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

spanning-tree portfast

!

interface GigabitEthernet1/13

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/14

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/15

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/16

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/17

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/18

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/19

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/20

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/21

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/22

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/23

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet1/24

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/1

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/2

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/3

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/4

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/5

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/6

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/7

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/8

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/9

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/10

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/11

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/12

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/13

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/14

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/15

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/16

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/17

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/18

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/19

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/20

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/21

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/22

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/23

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet2/24

no ip address

switchport

switchport trunk encapsulation dot1q

switchport trunk native vlan 30

switchport mode trunk

!

interface GigabitEthernet3/1

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/2

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/3

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/4

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/5

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/6

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/7

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/8

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/9

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/10

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/11

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/12

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/13

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/14

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/15

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/16

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/17

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/18

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/19

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/20

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/21

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/22

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/23

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/24

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/25

no ip address

mls qos trust dscp

switchport

switchport access vlan 220

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/26

no ip address

mls qos trust dscp

switchport

switchport access vlan 220

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/27

no ip address

mls qos trust dscp

switchport

switchport access vlan 220

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/28

no ip address

mls qos trust dscp

switchport

switchport access vlan 220

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/29

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/30

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/31

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/32

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/33

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/34

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/35

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/36

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/37

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/38

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/39

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/40

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/41

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/42

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/43

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/44

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/45

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/46

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/47

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet3/48

no ip address

mls qos trust dscp

switchport

switchport access vlan 10

switchport voice vlan 20

no mdix auto

spanning-tree portfast

!

interface GigabitEthernet4/1

no ip address

switchport

switchport access vlan 30

switchport mode access

spanning-tree portfast

!

interface GigabitEthernet4/2

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/3

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/4

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/5

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/6

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/7

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/8

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/9

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/10

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/11

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/12

no ip address

switchport

switchport access vlan 30

spanning-tree portfast

!

interface GigabitEthernet4/13

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/14

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/15

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/16

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/17

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/18

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/19

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/20

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/21

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/22

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/23

no ip address

switchport

switchport access vlan 20

spanning-tree portfast

!

interface GigabitEthernet4/24

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/25

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/26

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/27

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/28

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/29

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/30

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/31

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/32

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/33

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/34

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/35

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/36

no ip address

switchport

switchport access vlan 40

spanning-tree portfast

!

interface GigabitEthernet4/37

no ip address

switchport

switchport access vlan 80

spanning-tree portfast

!

interface GigabitEthernet4/38

no ip address

switchport

switchport access vlan 80

spanning-tree portfast

!

interface GigabitEthernet4/39

no ip address

switchport

switchport access vlan 80

spanning-tree portfast

!

interface GigabitEthernet4/40

no ip address

switchport

switchport access vlan 80

spanning-tree portfast

!

interface GigabitEthernet4/41

no ip address

switchport

switchport access vlan 80

spanning-tree portfast

!

interface GigabitEthernet4/42

no ip address

switchport

switchport access vlan 80

spanning-tree portfast

!

interface GigabitEthernet4/43

no ip address

switchport

switchport access vlan 100

spanning-tree portfast

!

interface GigabitEthernet4/44

no ip address

switchport

switchport access vlan 100

spanning-tree portfast

!

interface GigabitEthernet4/45

no ip address

switchport

switchport access vlan 100

spanning-tree portfast

!

interface GigabitEthernet4/46

no ip address

switchport

switchport access vlan 100

spanning-tree portfast

!

interface GigabitEthernet4/47

no ip address

switchport

switchport access vlan 100

switchport mode access

spanning-tree portfast

!

interface GigabitEthernet4/48

no ip address

switchport

switchport access vlan 100

switchport mode access

spanning-tree portfast

!

interface GigabitEthernet5/1

no ip address

switchport

!

interface GigabitEthernet5/2

no ip address

media-type rj45

switchport

switchport access vlan 100

spanning-tree portfast

!

interface GigabitEthernet6/1

no ip address

shutdown

!

interface GigabitEthernet6/2

no ip address

shutdown

!

interface Vlan1

no ip address

shutdown

!

interface Vlan10

no ip address

ip flow ingress

ip route-cache flow

!

interface Vlan20

no ip address

!

interface Vlan30

ip address 192.168.30.10 255.255.255.0

!

interface Vlan40

ip address 192.168.40.254 255.255.255.0

!

interface Vlan80

no ip address

!

interface Vlan100

no ip address

!

interface Vlan110

no ip address

!

ip default-gateway 192.168.30.1

ip classless

ip flow-export source Vlan10

ip flow-export destination 192.168.10.16 2055

ip http server

ip http access-class 10

ip http authentication local

!

!

logging trap debugging

logging 192.168.30.17

access-list 10 permit 192.168.30.12

access-list 10 permit 192.168.30.13

access-list 10 permit 192.168.30.10

!

snmp-server community Someone_private_com RW

snmp-server community Someone _public_com RO

snmp-server location Main Building NOC Room

snmp-server contact Myoffice

snmp-server enable traps snmp authentication linkdown linkup coldstart warmstart

snmp-server host 192.168.30.20 snmp

!

!

dial-peer cor custom

!

!

!

!

line con 0

line vty 0 4

password ************

line vty 5 15

password **************

!

!

monitor session 2 source interface Gi2/5

monitor session 2 filter vlan 80 , 100

monitor session 2 destination intrusion-detection-module 9 data-port 1

end