Upstream1                                                                     Upstream2

- My LAN block 192.168.52.0 /22 is successfully advertised through Upstream 1 .

- Now I introduced Upstream 2 and wanted only one /24 block – maybe 192.168.52.0/24 or 192.168.53.0/24 or 192.168.54.0/24 should pass through Upstream 2.

- I have noticed that unless and until I add “ ip route 192.168.52.0 255.255.255.0 Null0 “ route to the router the /24 block is not getting advertised out of the router to Upstream 2.

- Now as soon as I am adding that Null0 route , I cannot ping 192.168.52.1 / 22 interface and every other thing is getting wrong.

- The “ sh run” output of the switch running BGP process –

interface GigabitEthernet0/1

description Upstream1

no switchport

ip address 202.54.x.x 255.255.255.252

!

interface GigabitEthernet0/11

description Upstream2

no switchport

ip address 203.171.x.x 255.255.255.252

!

interface GigabitEthernet0/12

no switchport

ip address 192.168.52.1 255.255.252.0

!

router bgp @@@@@@

no synchronization

no bgp log-neighbor-changes

network 192.168.52.0 mask 255.255.255.0

network 192.168.53.0 mask 255.255.255.0

network 192.168.54.0 mask 255.255.255.0

network 192.168.55.0 mask 255.255.255.0

network 192.168.52.0 mask 255.255.252.0

neighbor 202.54.x.x1 remote-as @@@@@

neighbor 202.54.x.x1 route-map UPSTRM1 out

neighbor 203.171.x.x1 remote-as @@@@@

neighbor 203.171.x.x1 route-map UPSTRM2 out

no auto-summary

!

ip classless

ip route 0.0.0.0 0.0.0.0 202.54.x.x1

ip route 0.0.0.0 0.0.0.0 203.171.x.x1

ip route 192.168.52.0 255.255.252.0 Null0

ip route 192.168.53.0 255.255.255.0 Null0   <----------- This route is offending

!

ip prefix-list XYZ seq 25 permit 192.168.52.0/22

!

ip prefix-list ABC seq 55 permit 192.168.53.0/24

route-map UPSTRM1 permit 10

match ip address prefix-list XYZ

!

route-map UPSTRM2 permit 20

match ip address prefix-list ABC

!

# Text boxes

# Catalyst L3 Switch

( Cisco )

## Firewall- doing only Dynamic NAT

(Juniper)

192.168.52.1/22

192.168.55.254/22

Broadband Subscribers

WAN IP Block

203.171.x.x/30