Difference between HK to  Newyork with ringtone and HK to Tokyo with out

From HK to New York, Tokyo Output

Dec 18 17:22:18 UTC: ISDN Se0/1/0:15 Q931: TX -> SETUP pd = 8  callref = 0x04A4

Sending Complete

Bearer Capability i = 0x8090A3

Standard = CCITT

Transfer Capability = Speech

Transfer Mode = Circuit

Transfer Rate = 64 kbit/s

Channel ID i = 0xA98381

Exclusive, Channel 1

Facility i = 0x9FAA06800100820100A11F02010002010080174D61747473206C6F6E646F6E20746573742070686F6E65

Calling Party Number i = 0x0081, '7434161'

Plan:Unknown, Type:Unknown

Called Party Number i = 0x80, '7239621'

Plan:Unknown, Type:Unknown

Dec 18 17:22:19 UTC: ISDN Se0/1/0:15 Q931: RX <- CALL_PROC pd = 8  callref = 0x84A4

Channel ID i = 0xA98381

Exclusive, Channel 1

Dec 18 17:22:20 UTC: ISDN Se0/1/0:15 Q931: RX <- ALERTING pd = 8  callref = 0x84A4

Facility i = 0x9FAA06800100820100A1180201010201018010414D20554B20746573742070686F6E65

Progress Ind i = 0x8088 - In-band info or appropriate now available

Dec 18 17:22:26 UTC: ISDN Se0/1/0:15 Q931: TX -> DISCONNECT pd = 8  callref = 0x04A4

Cause i = 0x8190 - Normal call clearing

Dec 18 17:22:27 UTC: ISDN Se0/1/0:15 Q931: RX <- RELEASE pd = 8  callref = 0x84A4

Dec 18 17:22:27 UTC: ISDN Se0/1/0:15 Q931: TX -> RELEASE_COMP pd = 8  callref = 0x04A4

Fron Tokyo to New york, Tokyo Output

*Dec 18 17:03:47.029 UTC: ISDN Se1/1:23 Q931: RX <- SETUP pd = 8  callref = 0x00D5

Bearer Capability i = 0x8090A3

Standard = CCITT

Transer Capability = Speech

Transfer Mode = Circuit

Transfer Rate = 64 kbit/s

Channel ID i = 0xA98381

Exclusive, Channel 1

Facility i = 0x9FAA06800100820100A11F02010002010080174D61747473206C6F6E646F6E20746573742070686F6E65

Calling Party Number i = 0x0081, '7434161'

Plan:Unknown, Type:Unknown

Called Party Number i = 0x80, '1376'

Plan:Unknown, Type:Unknown

Sending Complete

*Dec 18 17:03:47.041 UTC: ISDN Se1/1:23 Q931: TX -> CALL_PROC pd = 8  callref = 0x80D5

Channel ID i = 0xA98381

Exclusive, Channel 1

*Dec 18 17:03:47.305 UTC: ISDN Se1/1:23 Q931: TX -> ALERTING pd = 8  callref = 0x80D5

TOKYO_10_2821_1#

*Dec 18 17:03:53.113 UTC: ISDN Se1/1:23 Q931: RX <- DISCONNECT pd = 8  callref = 0x00D5

Cause i = 0x8190 - Normal call clearing

*Dec 18 17:03:53.113 UTC: ISDN Se1/1:23 Q931: TX -> RELEASE pd = 8  callref = 0x80D5

*Dec 18 17:03:53.433 UTC: ISDN Se1/1:23 Q931: RX <- RELEASE_COMP pd = 8  callref = 0x00D5

TOKYO_10_2821_1#

Difference between HK to New York with ringtone and HK to Tokyo with out ringtone.

From Hk to New york, HK output

Dec 18 17:10:09 UTC: ISDN Se0/1/0:15 Q931: TX -> SETUP pd = 8  callref = 0x04A1

Sending Complete

Bearer Capability i = 0x8090A3

Standard = CCITT

Transfer Capability = Speech

Transfer Mode = Circuit

Transfer Rate = 64 kbit/s

Channel ID i = 0xA98381

Exclusive, Channel 1

Facility i = 0x9FAA06800100820100A11F02010002010080174D61747473206C6F6E646F6E20746573742070686F6E65

Calling Party Number i = 0x0081, '7434161'

Plan:Unknown, Type:Unknown

Called Party Number i = 0x80, '7239621'

Plan:Unknown, Type:Unknown

Dec 18 17:10:10 UTC: ISDN Se0/1/0:15 Q931: RX <- CALL_PROC pd = 8  callref = 0x84A1

Channel ID i = 0xA98381

Exclusive, Channel 1

Dec 18 17:10:11 UTC: ISDN Se0/1/0:15 Q931: RX <- ALERTING pd = 8  callref = 0x84A1

Facility i = 0x9FAA06800100820100A1180201010201018010414D20554B20746573742070686F6E65

Progress Ind i = 0x8088 - In-band info or appropriate now available

Dec 18 17:10:16 UTC: ISDN Se0/1/0:15 Q931: TX -> DISCONNECT pd = 8  callref = 0x04A1

Cause i = 0x8290 - Normal call clearing

Dec 18 17:10:17 UTC: ISDN Se0/1/0:15 Q931: RX <- RELEASE pd = 8  callref = 0x84A1

Dec 18 17:10:17 UTC: ISDN Se0/1/0:15 Q931: TX -> RELEASE_COMP pd = 8  callref = 0x04

From HK to Tokyo, HK output

Dec 18 17:10:31 UTC: ISDN Se0/1/0:15 Q931: TX -> SETUP pd = 8  callref = 0x04A2

Sending Complete

Bearer Capability i = 0x8090A3

Standard = CCITT

Transfer Capability = Speech

Transfer Mode = Circuit

Transfer Rate = 64 kbit/s

Channel ID i = 0xA98381

Exclusive, Channel 1

Facility i = 0x9FAA06800100820100A11F02010002010080174D61747473206C6F6E646F6E20746573742070686F6E65

Calling Party Number i = 0x0081, '7434161'

Plan:Unknown, Type:Unknown

Called Party Number i = 0x80, '7451376'

Plan:Unknown, Type:Unknown

Dec 18 17:10:32 UTC: ISDN Se0/1/0:15 Q931: RX <- CALL_PROC pd = 8  callref = 0x84A2

Channel ID i = 0xA98381

Exclusive, Channel 1

Dec 18 17:10:32 UTC: ISDN Se0/1/0:15 Q931: RX <- ALERTING pd = 8  callref = 0x84A2

Dec 18 17:10:40 UTC: ISDN Se0/1/0:15 Q931: TX -> DISCONNECT pd = 8  callref = 0x04A2

Cause i = 0x8290 - Normal call clearing

Dec 18 17:10:41 UTC: ISDN Se0/1/0:15 Q931: RX <- RELEASE pd = 8  callref = 0x84A2

Dec 18 17:10:41 UTC: ISDN Se0/1/0:15 Q931: TX -> RELEASE_COMP pd = 8  callref = 0x04A2