Branch Router –

crypto isakmp policy 10

authentication pre-share

group 2

crypto isakmp key cisco address 172.255.0.1

!

!

crypto ipsec transform-set BEL-Set esp-des esp-sha-hmac

mode transport

!

crypto map BEL-Map 1 ipsec-isakmp

set peer 172.255.0.1

set transform-set BEL-Set

match address 116

!

access-list 116 permit ip 172.209.0.0 0.0.255.255 128.200.0.0 0.0.255.255

!

interface Dialer1

description "*****Connected to GAD*****"

ip address 172.223.1.2 255.255.255.252

encapsulation ppp

dialer in-band

dialer idle-timeout 180

dialer map ip 172.223.1.1 name BEL-GAD broadcast 01202775453

dialer load-threshold 50 either

dialer-group 1

ppp authentication chap

ppp multilink

crypto map BEL-Map

!

router ospf 100

log-adjacency-changes

network 172.209.1.1 0.0.0.0 area 3

network 172.223.0.2 0.0.0.0 area 3

network 172.223.100.2 0.0.0.0 area 3

!

ip classless

ip route 128.200.0.0 255.255.0.0 172.223.1.1 200

ip route 172.223.1.0 255.255.255.252 Dialer1

ip route 172.255.0.0 255.255.255.252 172.223.1.1 200

ip route 172.255.1.0 255.255.255.252 172.223.1.1 200

!

Aggregation Point Router –

!

interface Dialer2

description "*****Connected to PK*****"

ip address 172.223.1.1 255.255.255.252

encapsulation ppp

delay 500000

dialer pool 1

dialer remote-name BEL-PK

dialer idle-timeout 180

dialer-group 1

ppp authentication chap

ppp multilink

!

router ospf 100

log-adjacency-changes

redistribute connected subnets

redistribute static subnets

network 80.200.0.1 0.0.0.0 area 3

network 172.223.0.1 0.0.0.0 area 3

network 172.223.0.4 0.0.0.3 area 3

network 172.223.0.9 0.0.0.0 area 3

network 172.223.0.12 0.0.0.3 area 3

network 172.223.0.17 0.0.0.0 area 3

network 172.223.1.1 0.0.0.0 area 3

network 172.223.1.5 0.0.0.0 area 3

network 172.223.1.9 0.0.0.0 area 3

network 172.223.1.13 0.0.0.0 area 3

network 172.223.1.17 0.0.0.0 area 3

network 172.223.100.1 0.0.0.0 area 3

network 172.255.0.2 0.0.0.0 area 0

network 172.255.0.37 0.0.0.0 area 0

network 172.255.1.2 0.0.0.0 area 0

network 172.255.1.37 0.0.0.0 area 0

!

DCR1 –

!

crypto isakmp policy 10

authentication pre-share

group 2

crypto isakmp key cisco address 172.223.1.2

!

!

crypto ipsec transform-set BEL-Set esp-des esp-sha-hmac

mode transport

!

!

!

!

crypto map BEL-Map 1 ipsec-isakmp

set peer 172.223.1.2

set transform-set BEL-Set

match address 116

!

!

interface Serial0/0/0

description ****Connected to Gadiabad****

bandwidth 2048

no ip address

encapsulation ppp

invert txclock

ppp multilink

ppp multilink group 1

crypto map BEL-Map

!

router ospf 100

log-adjacency-changes

redistribute static subnets

network 172.255.0.1 0.0.0.0 area 0

!

access-list 116 permit ip 128.200.0.0 0.0.255.255 172.209.0.0 0.0.255.255

!