Site B Configs.

SiteB_1841#sh run

Building configuration...

Current configuration : 3989 bytes

!

version 12.3

no service pad

service tcp-keepalives-in

service tcp-keepalives-out

service timestamps debug datetime msec

service timestamps log datetime msec

service password-encryption

!

hostname SiteB_1841

!

boot-start-marker

boot system flash:c1841-entbase-mz.123-8.T11.bin

boot-end-marker

!

logging buffered 51200 warnings

!

clock timezone FIJI 12

mmi polling-interval 60

no mmi auto-configure

no mmi pvc

mmi snmp-timeout 180

aaa new-model

!

!

aaa authentication ppp default none

aaa authentication ppp DDR local

aaa session-id common

ip subnet-zero

ip cef

!

!

ip tcp timestamp

ip tcp synwait-time 300

ip tcp path-mtu-discovery

!

!

ip flow-cache timeout active 1

no ip bootp server

no ip domain lookup

no ftp-server write-enable

isdn switch-type basic-net3

!

username SiteA_1841 password 7 1446415E55

!

!

!

interface Loopback0

description Loopback 0

ip address 160.8.253.86 255.255.255.255

!

interface FastEthernet0/0

description SiteB LAN

ip address 160.8.86.20 255.255.255.0

speed 100

full-duplex

!

interface FastEthernet0/1

description Link to SWX 2

no ip address

speed 100

full-duplex

!

interface Serial0/0/0

description 128Kbps TFL LL to SiteA

bandwidth 128

ip address 160.8.200.142 255.255.255.252

no keepalive

priority-group 1

!

interface Serial0/0/1

no ip address

shutdown

clockrate 2000000

!

interface BRI0/1/0

description ISDN Backup to SiteA

bandwidth 128

no ip address

encapsulation ppp

no ip route-cache cef

no ip route-cache

no ip mroute-cache

dialer pool-member 1

isdn switch-type basic-net3

no keepalive

no fair-queue

ppp authentication chap

!

interface Dialer1

ip address 160.8.200.146 255.255.255.252

no ip redirects

no ip proxy-arp

encapsulation ppp

no ip route-cache cef

no ip route-cache

no ip mroute-cache

shutdown

dialer pool 1

dialer remote-name SiteA_1841

dialer string 3302691

dialer-group 1

no cdp enable

ppp authentication chap

!

router eigrp 5

network 160.8.0.0

no auto-summary

!

ip classless

ip route 0.0.0.0 0.0.0.0 160.8.85.44

ip route 0.0.0.0 0.0.0.0 Serial0/0/0

ip route 10.254.4.0 255.255.255.0 BRI0/1/0 250

ip route 160.8.9.0 255.255.255.0 BRI0/1/0 250

ip route 160.8.10.0 255.255.255.0 BRI0/1/0 250

ip route 160.8.24.0 255.255.255.0 BRI0/1/0 250

ip route 160.8.27.0 255.255.255.0 BRI0/1/0 250

ip route 160.8.28.0 255.255.255.0 BRI0/1/0 250

ip route 160.8.30.0 255.255.255.0 BRI0/1/0 250

ip route 160.8.32.0 255.255.252.0 BRI0/1/0 250

ip route 160.8.60.0 255.255.252.0 BRI0/1/0 250

ip route 160.8.85.0 255.255.255.0 BRI0/1/0 250

no ip http server

!

!

access-list 101 permit tcp any host 160.8.24.43

access-list 105 permit ip any any

dialer-list 1 protocol ip permit

priority-list 1 protocol ip high list 101

priority-list 1 protocol ip normal list 105

snmp-server ifindex persist

snmp-server enable traps snmp authentication linkdown linkup coldstart warmstart

snmp-server enable traps tty

snmp-server host 160.8.32.42

!

!

!

control-plane

!

banner motd ^C

Site B router

AUTHORISED ACCESS ONLY!!!

^C

!

line con 0

password 7 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxx

transport preferred telnet

transport output all

line aux 0

line vty 0 4

exec-timeout 0 0

password 7 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx

transport preferred telnet

transport input none

transport output all

line vty 5 15

password 7 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx

!

scheduler allocate 20000 1000

ntp server 160.8.85.20

end

SiteB_1841#

Site A Configs

SiteA_1841>en

Password:

SiteA_1841#sh run

Building configuration...

Current configuration : 4097 bytes

!

version 12.3

service timestamps debug datetime msec

service timestamps log datetime msec

service password-encryption

!

hostname SiteA_1841

!

boot-start-marker

boot system flash:c1841-entbase-mz.123-8.T11.bin

boot system flash:

boot-end-marker

!

logging buffered 51200 warnings

!

clock timezone Fiji 12

mmi polling-interval 60

no mmi auto-configure

no mmi pvc

mmi snmp-timeout 180

aaa new-model

!

!

aaa authentication ppp default none

aaa session-id common

ip subnet-zero

ip cef

!

!

ip tcp path-mtu-discovery

!

!

ip flow-cache timeout active 1

no ftp-server write-enable

isdn switch-type basic-net3

!

username SiteB_1841 password 7 005540535D

!

!

track 1 rtr 1 reachability

delay down 5 up 20

!

!

interface Loopback0

description Loopback 0

ip address 160.8.253.85 255.255.255.255

!

interface FastEthernet0/0

description Site A LAN

ip address 160.8.85.20 255.255.255.0

ip route-cache flow

speed 100

full-duplex

!

interface FastEthernet0/1

no ip address

shutdown

duplex auto

speed auto

!

interface Serial0/0/0

description Service Provider local Loop

bandwidth 128

ip address 10.254.4.1 255.255.255.252

ip route-cache flow

no keepalive

!

interface Serial0/0/1

description 128Kbps LL to SiteB

bandwidth 128

ip address 160.8.200.141 255.255.255.252

no keepalive

!

interface BRI0/1/0

description ISDN Backup to SiteB

bandwidth 128

no ip address

encapsulation ppp

load-interval 30

dialer pool-member 1

isdn switch-type basic-net3

no fair-queue

no cdp enable

ppp authentication chap

!

interface Dialer0

no ip address

!

interface Dialer1

ip address 160.8.200.145 255.255.255.252

no ip redirects

no ip proxy-arp

encapsulation ppp

shutdown

dialer pool 1

dialer remote-name bspnadi_1841

dialer string 6705115

dialer-group 1

no cdp enable

ppp authentication chap

!

router eigrp 5

network 160.8.0.0

no auto-summary

!

ip classless

ip route 160.8.0.0 255.255.0.0 10.254.4.2 track 1

ip route 0.0.0.0 0.0.0.0 160.8.85.44

ip route 10.254.4.0 255.255.255.0 10.254.4.2

ip route 160.8.0.0 255.255.0.0 160.8.85.44 200

ip route 160.8.86.0 255.255.255.0 BRI0/1/0 250

ip flow-export source FastEthernet0/0

ip flow-export version 5

ip flow-export destination 160.8.32.42 9996

no ip http server

!

!

access-list 101 permit tcp any host 160.8.10.8

access-list 101 permit tcp any host 160.8.24.15

access-list 101 permit tcp any host 160.8.10.3

access-list 101 permit tcp any host 160.8.10.43

access-list 101 permit tcp any host 160.8.24.43

access-list 105 permit ip any any

dialer-list 1 protocol ip permit

priority-list 1 protocol ip high list 101

priority-list 1 protocol ip normal list 105

snmp-server ifindex persist

snmp-server enable traps snmp authentication linkdown linkup coldstart warmstart

snmp-server enable traps tty

snmp-server enable traps syslog

snmp-server host 160.8.32.42

!

!

!

control-plane

!

rtr 1

type echo protocol ipIcmpEcho 10.254.4.10

rtr schedule 1 life forever start-time now

banner motd ^C

Site A Router.

AUTHORISED ACCESS ONLY!!! ^C

!

line con 0

password 7 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx

transport preferred telnet

transport output all

line aux 0

line vty 0 4

exec-timeout 0 0

password 7 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx

transport preferred telnet

transport input all

transport output all

line vty 5 15

password 7 xxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx

!

scheduler allocate 20000 1000

end

SiteA_1841#