Basic Load Balancing Using Routed Mode on the Cisco Application Control Engine

### Goal

Configure basic load balancing (Layer 3) where client traffic enters on one network and is directed to servers residing on a second network.

### Design

Clients will send application requests through the multilayer switch feature card (MSFC), which routes them to a virtual IP address (VIP) within the Cisco® Application Control Engine (ACE). The VIP used in this example resides in an ACE context, which is configured with a client VLAN and a server VLAN (Figure 1). Client requests will arrive at the VIP, and the ACE will pick the appropriate server and then use the destination Network Address Translation (NAT) to send the client request to the server. The server will respond using the interface VLAN of the ACE as its default gateway to the client. The ACE will then change the source IP to be the VIP and forward the response to the client via the MSFC.

Example of a Network Topology Using a Cisco Application Control Engine

### Configuration

The Cisco ACE needs to be configured via access control lists (ACLs) to allow traffic into the ACE data plane. After the ACL checks are made, a service policy, which is applied to the interface, is used to classify traffic destined for the VIP. The VIP is associated with a load-balancing action within the multimatch policy. The load-balancing action tells the ACE how to handle traffic that has been directed to a VIP. In this example, all traffic is sent to a server farm, where it is distributed in round-robin fashion to one of five real servers. The ACE configuration occurs in layers, such that it builds from the real IPs to applying the VIP on an interface. Due to this layered structure, it is optimal to create the configuration by working backward from the way the flow is processed. Thus, to enable server load balancing you need to do the following:

Enable ACLs to allow data traffic through the ACE device, as it is denied by default.

Configure the IPs of the servers (define rservers).

Group the real servers (create a server farm).

Define the virtual IP address (VIP).

Define how traffic is to be handled as it is received (create a policy map for load balancing).

Associate a VIP to a handling action (create a multimatch policy map [a service policy])

Create client- and server-facing interfaces.

Apply the VIP and ACL permitting client connections to the interface (apply access group and service policy to interface).

To begin the configuration, create an access list for permitting client connections.

ACE-1/routed(config)# access-list everyone extended permit ip any any

ACE-1/routed(config)# access-list everyone extended permit icmp any any

Although this example shows a “permit any any,” it is recommended that ACLs be used to permit only the traffic you want allow through the Cisco ACE. In the past, server load-balancing (SLB) devices have used the VIP and port alone to protect servers. Within the ACE, ACLs are processed first, and thus dropping traffic using an ACL requires fewer resources than dropping it once it passes the ACLs and reaches the VIP.

The Cisco ACE needs to know the IP address of the servers available to handle client connections. The rserver command is used to define the IP address of the service. In addition, each rserver must be place in service for it to be used. The benefit of this design is that no matter how many applications or services an rserver hosts, the entire real server can be completely removed from the load-balancing rotation by issuing a single “no inservice” or “no inservice-standby” command at the rserver level. This is very beneficial for users needing to upgrade or patch an rserver, because they no longer have to go to each application and remove each instance of the rserver.

ACE-1/routed(config)# rserver lnx1

ACE-1/routed(config-rserver-host)# ip add 192.168.1.11

ACE-1/routed(config-rserver-host)# inservice

ACE-1/routed(config-rserver-host)# rserver lnx2

ACE-1/routed(config-rserver-host)# ip add 192.168.1.12

ACE-1/routed(config-rserver-host)# inservice

ACE-1/routed(config-rserver-host)# rserver lnx3

ACE-1/routed(config-rserver-host)# ip add 192.168.1.13

ACE-1/routed(config-rserver-host)# inservice

ACE-1/routed(config-rserver-host)# rserver lnx4

ACE-1/routed(config-rserver-host)# ip add 192.168.1.14

ACE-1/routed(config-rserver-host)# inservice

ACE-1/routed(config-rserver-host)# rserver lnx5

ACE-1/routed(config-rserver-host)# ip add 192.168.1.15

ACE-1/routed(config-rserver-host)# inservice

Now group the rservers to be used to handle client connections into a server farm. Again, the rserver must be placed in service. This allows a single instance of an rserver to be manually removed from rotation.

ACE-1/routed(config-cmap)# serverfarm web

ACE-1/routed(config-sfarm-host)# rserver lnx1

ACE-1/routed(config-sfarm-host-rs)# inservice

ACE-1/routed(config-sfarm-host-rs)# rserver lnx2

ACE-1/routed(config-sfarm-host-rs)# inservice

ACE-1/routed(config-sfarm-host-rs)# rserver lnx3

ACE-1/routed(config-sfarm-host-rs)# inservice

ACE-1/routed(config-sfarm-host-rs)# rserver lnx4

ACE-1/routed(config-sfarm-host-rs)# inservice

ACE-1/routed(config-sfarm-host-rs)# rserver lnx5

ACE-1/routed(config-sfarm-host-rs)# inservice

Use a class map to define the VIP to which clients will send their requests. In this example, the VIP is considered L3 (Layer 3) because there is a match on any port. If the VIP were to match only HTTP traffic, the match would be bound to port 80 and considered an L4 (Layer 4) VIP. (For example, “match virtual-address 172.16.1.100 tcp eq 80”).

ACE-1/routed(config)# class-map slb-vip

ACE-1/routed(config-cmap)# match virtual-address 172.16.1.100 any

Next define the action to take when a new client request arrives. In this case, all traffic will be sent to the “web” serverfarm. This type of load balancing is considered L4 since only class-default is used.

ACE-1/routed(config)# policy-map type loadbalance http first-match slb

ACE-1/routed(config-pmap-lb)# class class-default

ACE-1/routed(config-pmap-lb-c)# serverfarm web

Since the VIPs and load-balancing actions are defined independently, they must be associated so that the Cisco ACE knows how to handle traffic destined for a VIP. The association is made using a multimatch policy map. Keep in mind that multimatch policy maps are applied to interfaces as service policies.

ACE-1/routed(config)# policy-map multi-match client-vips

ACE-1/routed(config-pmap)# class slb-vip

ACE-1/routed(config-pmap-c)# loadbalance policy slb

ACE-1/routed(config-pmap-c)# loadbalance vip inservice

At this point the interface VLANs can be created to interconnect the Cisco ACE to the client side of the network and to the servers.

ACE-1/routed(config)# interface vlan 20

ACE-1/routed(config-if)# description “Client Side”

ACE-1/routed(config-if)# ip address 172.16.1.5 255.255.255.0

ACE-1/routed(config-if)# no shutdown

ACE-1/routed(config-if)# interface vlan 40

ACE-1/routed(config-if)# description “Default gateway of real servers”

ACE-1/routed(config-if)# ip address 192.168.1.1 255.255.255.0

ACE-1/routed(config-if)# no shutdown

The last step is to apply the ACL and service policy (“policy-map multi-match”) to the client-side interface. Both the access group and service policy are applied on the input side of the interface.

ACE-1/routed(config)# interface vlan 20

ACE-1/routed(config-if)# access-group input everyone

ACE-1/routed(config-if)# service-policy input client-vips

There is no need to add an access group to the server side, as the Cisco ACE automatically creates pinholes to allow server response traffic to pass back to the client.

### Related “show” Commands

ACE-1/routed #show arp

ACE-1/routed #show acl

ACE-1/routed #show service-policy client-vips

ACE-1/routed #show serverfarm

ACE-1/routed #show rserver

ACE-1/routed #show stats

### Comments

Once you’ve completed the configuration, verify that the Cisco ACE has an Address Resolution Protocol (ARP) response for each rserver and the default route to the client. Check the ACL hits to ensure that client connections are being accepted. Check the service policy output to see the client connection hits, and verify that the server is responding with response packets. The “show” command for serverfarm and rserver can be used to display the exact rserver handling the connection and the amount of work the entire server farm has handled. The “show stats” command provides a higher level of monitoring of ACE load balancing, inspection, probes, and other important metrics.

### show running-config

ACE-1/routed# show run

access-list everyone line 8 extended permit ip any any

access-list everyone line 16 extended permit icmp any any

rserver host lnx1

ip address 192.168.1.11

inservice

rserver host lnx2

ip address 192.168.1.12

inservice

rserver host lnx3

ip address 192.168.1.13

inservice

rserver host lnx4

ip address 192.168.1.14

inservice

rserver host lnx5

ip address 192.168.1.15

inservice

serverfarm host web

rserver lnx1

inservice

rserver lnx2

inservice

rserver lnx3

inservice

rserver lnx4

inservice

rserver lnx5

inservice

class-map match-all slb-vip

2 match virtual-address 172.16.1.100 any

policy-map type management first-match remote-access

class class-default

permit

policy-map type loadbalance http first-match slb

class class-default

serverfarm web

policy-map multi-match client-vips

class slb-vip

loadbalance vip inservice

loadbalance policy slb

interface vlan 20

description "Client Side"

ip address 172.16.1.5 255.255.255.0

access-group input everyone

service-policy input client-vips

no shutdown

interface vlan 40

description "Default gateway of real servers"

ip address 192.168.1.1 255.255.255.0

service-policy input remote-access

no shutdown

ip route 0.0.0.0 0.0.0.0 172.16.1.1

# Text boxes

Printed in USA	C78-331727-01   10/08

VLAN 40

VLAN 20

192.168.1. 1

192.168.1.14

192.168.1.12

Internet

ACE

172.16.1. 1

192.168.1.15

192.168.1.13

Int:  172.16.1.5

VIP: 172.16.1.100

192.168.1.11

MSFC

Client

209.165.201.10

Servers