| Table 28-2 Media Termination Point Types |
| --- |
| MTP Type | Description |
| Cisco IOS Enhanced Media Termination Point | This type supports Cisco 2600XM, Cisco 2691, Cisco 3725, Cisco 3745, and Cisco 3660 Access Routers and the following MTP cases: For software-only implementation that does not use DSP but has the same packetization time for devices that support G.711 to G.711 or G.729 to G.729 codecs, this implementation can support up to 500 sessions per gateway. For a hardware-only implementation with DSP for devices that use G.711, G.729a, and G.729b codecs, 200 sessions can occur per NM-HDV2, and 48 sessions can occur per NM-HD. Note : For more information on using G.729 codecs over SIP trunks, see Understanding Session Initiation Protocol (SIP). This type can support Network Address Translation in a service provider environment to hide the private address. In Cisco Unified Communications Manager Administration, ensure that you enter the same MTP name that exists in the gateway Command Line Interface (CLI). Refer to the "Configuring Enhanced Conferencing and Transcoding for Voice Gateway Routers" section of the Cisco Unified Communications Manager and Cisco IOS Interoperability Configuration Guide for more information. |