Use an SSH client (suck as Putty) to ssh to the IP 172.16.17.50

username: flt

password: rtoflt

[flt@cwitplnagios ~]$ telnet 203.169.57.86

password: f15htank5

enable password: cisco

foxconn-gw#sh run

Building configuration...

Current configuration : 6005 bytes

!

! Last configuration change at 11:30:51 UTC Fri Apr 9 2010

!

version 12.4

service timestamps debug datetime msec

service timestamps log datetime msec

ip tftp source-interface Loopback1

ip domain name cw.net

ip name-server XX.XX.XX.XX

ip name-server XX.XX.XX.XX

ip name-server XX.XX.XX.XX

ip rcmd rcp-enable

ip rcmd rsh-enable

ip rcmd remote-host rtrswcfg XX.XX.XX.XX rtrswcfg enable

ip rcmd source-interface Loopback1

isdn switch-type primary-qsig

!

voice-card 0

no dspfarm

controller E1 0/0/0

framing NO-CRC4

pri-group timeslots 1-31

description <E1/PRI CONNECTION TO CUSTOMER PBX>

controller E1 0/0/1

!

translation-rule 1

Rule 1 any XXXXXXXX ANY international

!

!

translation-rule 2

Rule 1 any XXXXXXXX ANY international

!

!

!

!

interface Loopback1

description

ip address XX.XX.XX.XX 255.255.255.255

!

interface GigabitEthernet0/0

no ip address

shutdown

duplex auto

speed auto

!

interface GigabitEthernet0/1

description

ip address XX.XX.XX.XX 255.255.255.252

ip access-group 103 in

duplex full

speed 100

h323-gateway voip interface

h323-gateway voip h323-id TEST

h323-gateway voip bind srcaddr XX.XX.XX.XX

!

interface Serial0/0/0:15

no ip address

encapsulation hdlc

no logging event link-status

isdn switch-type primary-qsig

isdn protocol-emulate network

isdn incoming-voice voice

isdn T310 120000

no cdp enable

!

ip route 0.0.0.0 0.0.0.0 XX.XX.XX.XX

ip route XX.XX.XX.XX 255.255.255.255 XX.XX.XX.XX

ip route XX.XX.XX.XX 255.255.255.255 XX.XX.XX.XX

!

!

no ip http server

no ip http secure-server

!

any any

!

control-plane

!

!

!

voice-port 0/0/0:15

translate calling 1

timeouts interdigit 2

description "QSIG Signalling with PBX"

!

!

!

!

!

dial-peer voice 1000 voip

destination-pattern .T

session target ipv4: XX.XX.XX.XX

dtmf-relay cisco-rtp

no vad

!

dial-peer voice 1 pots

destination-pattern 9T

direct-inward-dial

port 0/0/0:15

forward-digits all

!

!

Cisco 2851 (revision 53.51) with 249856K/12288K bytes of memory.

Processor board ID XXXXX

2 Gigabit Ethernet interfaces

31 Serial interfaces

2 Channelized E1/PRI ports

DRAM configuration is 64 bits wide with parity enabled.

239K bytes of non-volatile configuration memory.

62720K bytes of ATA CompactFlash (Read/Write)

Configuration register is 0x2102

# Text boxes

:

,

11

,

:

-

1

-

:

.

1

.

IP Network

Managed

2851

CE

Router

E

1

Call Server

International TDM Network

DIA PoP

TDM PBX

(

Nortel

11

C

)

2

M Port

10

M Ethernet

V

Physical Diagram

/

0

.

.

.

/

30

GigE

0

/

1

.

.

.

/

30

.

.

.

.

.

.

1

: