ClarkCounty#sh run

Building configuration...

Current configuration : 12577 bytes

!

! Last configuration change at 11:57:42 pdt Wed Jun 30 2010 by lvccld

! NVRAM config last updated at 08:10:54 pdt Mon Jun 28 2010 by lvccld

!

upgrade fpd auto

version 12.4

no service pad

service timestamps debug uptime

service timestamps log datetime msec localtime show-timezone

service password-encryption

!

hostname ClarkCounty

!

boot-start-marker

boot-end-marker

!

logging exception 4096

logging count

logging console informational

logging monitor informational

enable secret 5 $1$Dpfc$S0VDiBevOQP.GGfO7GMoO/

!

aaa new-model

!

!

aaa authentication login default local

!

!

aaa session-id common

clock timezone pst -8

clock summer-time pdt recurring

no ip source-route

ip cef

!

!

!

!

no ip domain lookup

ip domain name lvccld.org

ip host internet x.x.111.1

ip dhcp-server x.x.64.8

!

multilink bundle-name authenticated

!

!

!

!

!

!

!

!

!

!

!

!

!

!

!

!

archive

log config

hidekeys

!

!

ip ssh authentication-retries 2

ip ssh version 1

!

!

!

!

interface FastEthernet0/0

no ip address

duplex auto

speed auto

!

!

interface FastEthernet0/1

description Vacant port

no ip address

duplex full

speed auto

!

interface ATM1/0

description 60.HIDA.261580 ATM/OC3

no ip address

map-group CCLD

no atm ilmi-keepalive

!

interface ATM1/0.13 point-to-point

description LAUGHLIN 60.QRDA.314261

mtu 1500

ip address x.x.161.65 255.255.255.252

no snmp trap link-status

pvc 4/68

vbr-rt 1536 1536

encapsulation aal5snap

!

!

interface ATM1/0.14 point-to-point

description TO MESQUITE 60.QRDA.350231

mtu 1500

ip address x.x.161.69 255.255.255.252

no snmp trap link-status

pvc 4/50

vbr-rt 1536 1536

encapsulation aal5snap

!

!

interface ATM1/0.16 point-to-point

description MOAPA  60.QEZA.287743

mtu 1500

ip address x.x.161.73 255.255.255.252

no snmp trap link-status

pvc 4/67

vbr-rt 1536 1536

encapsulation aal5snap

!

!

interface ATM1/0.17 point-to-point

description Overton NEW circuit 60.QRDA.349576

mtu 1500

ip address x.x.161.77 255.255.255.252

no snmp trap link-status

pvc 4/45

vbr-rt 1536 1536

encapsulation aal5snap

!

!

interface ATM1/0.19 point-to-point

description SANDY VALLEY  60.QEZA.266033

mtu 1500

ip address x.x.161.85 255.255.255.252

no snmp trap link-status

pvc 4/42

vbr-rt 1536 1536

encapsulation aal5snap

!

!

interface ATM1/0.20 point-to-point

description INDIAN SPRINGS  60.QEZA.266027

mtu 1500

ip address x.x.161.61 255.255.255.252

no snmp trap link-status

pvc 4/46

vbr-rt 1536 1536

encapsulation aal5snap

!

!

interface ATM1/0.21 point-to-point

description SEARCHLIGHT  60.QEZA.265490

mtu 1500

ip address x.x.161.89 255.255.255.252

no snmp trap link-status

pvc 4/64

vbr-rt 1536 1536

encapsulation aal5snap

!

!

interface ATM1/0.23 point-to-point

description Blue Diamond 60.QGXX.264468

mtu 1500

ip address x.x.161.49 255.255.255.252

no snmp trap link-status

pvc 4/49

vbr-rt 1536 1536

encapsulation aal5snap

!

!

interface ATM1/0.47 point-to-point

description GOODSPRINGS 60.QEZA.264901

mtu 1500

ip address x.x.161.57 255.255.255.252

no snmp trap link-status

pvc 4/47

vbr-rt 1536 1536

encapsulation aal5snap

!

!

interface FastEthernet2/0

ip address x.x.64.2 255.255.255.0

duplex full

!

interface FastEthernet2/1

description Public WiFi Access

no ip address

no ip route-cache cef

no ip route-cache

duplex full

!

interface FastEthernet2/1.11

encapsulation dot1Q 11

ip address 10.32.11.1 255.255.255.0

ip access-group 198 in

no ip route-cache

!

interface FastEthernet2/1.12

description SUPERNETTED TO 10.32.12.1 THROUGH 10.32.13.254

encapsulation dot1Q 12

ip address 10.32.12.1 255.255.254.0

ip access-group 197 in

no ip route-cache

!

router eigrp 100

redistribute static

network 10.0.0.0

network x.x.2.0

network x.x.161.56 0.0.0.3

network x.x.161.0

network x.x.64.0

network x.x.76.0

network x.x.77.0

network x.x.78.0

network x.x.96.0

no auto-summary

no eigrp log-neighbor-changes

!

ip route 0.0.0.0 0.0.0.0 x.x.64.12

ip route 10.2.3.0 255.255.255.0 x.x.64.3

ip route 10.2.4.0 255.255.255.0 x.x.64.3

ip route x.x.70.0 255.255.255.0 192.168.2.70

ip route x.x.79.0 255.255.255.0 192.168.2.79

ip route x.x.88.0 255.255.255.0 192.168.2.88

ip route x.x.98.0 255.255.255.0 192.168.2.98

ip route x.x.99.0 255.255.255.0 192.168.2.99

ip route x.x.100.0 255.255.255.0 192.168.2.100

ip route x.x.101.0 255.255.255.0 192.168.2.101

ip route x.x.102.0 255.255.255.0 192.168.2.102

ip route x.x.104.0 255.255.255.0 192.168.2.104

ip route x.x.105.0 255.255.255.0 192.168.2.101

ip route x.x.106.0 255.255.255.0 192.168.2.106

ip route x.x.107.0 255.255.255.0 192.168.2.107

ip route x.x.108.0 255.255.255.0 192.168.2.100

no ip http server

ip http authentication local

no ip http secure-server

!

ip flow-export version 5

!

!

ip access-list extended FS_ACL

permit ip any any

!

ip sla 100

icmp-echo x.x.106.1 source-ip x.x.64.2

request-data-size 24

tos 30

timeout 60000

threshold 200

owner OpManager

history statistics-distribution-interval 20

ip sla reaction-configuration 100 react rtt threshold-value 200 150 threshold-type immediate action-type trapOnly

ip sla reaction-configuration 100 react connectionLoss threshold-type immediate action-type trapOnly

ip sla reaction-configuration 100 react timeout threshold-type immediate action-type trapOnly

ip sla reaction-configuration 100 react verifyError threshold-type immediate action-type trapOnly

ip sla schedule 100 life forever start-time pending ageout 60

ip sla 101

path-echo x.x.106.1 source-ip x.x.64.2

request-data-size 24

tos 30

timeout 60000

threshold 200

owner OpManager

paths-of-statistics-kept 2

hops-of-statistics-kept 15

ip sla schedule 101 life forever start-time 14:46:06 Jul 19 ageout 3600

!

map-list CCLD

ip 198.147.161.1 atm-vc 11 broadcast

ip 198.147.161.2 atm-vc 11 broadcast

logging alarm informational

logging trap debugging

logging source-interface FastEthernet2/0

!

!

!

!

!

!

control-plane

!

!

!

!

dial-peer cor custom

!

!

!

!

gatekeeper

shutdown

!

banner motd ^C

Warning!!! Warning !!! Warning !!! Warning !!! Warning !!!

This system is solely for the use of authorized users for official purposes.

If you are about to make configuration change to this device, please ensure

to send a "Tech Note". You have no expectation of privacy in its use and to

ensure that the system is functioning properly, individuals using this system

are subject to having all of their activities monitored and recorded by

system personnel. Use of this system evidences an express consent to such

monitoring and agreement that if such monitoring reveals evidence of possible

abuse or criminal activity, system personnel may provide the results of such

monitoring to the appropriate officials.

^C

!

line con 0

exec-timeout 30 0

password 7 110A1A5413435A5C52

logging synchronous

stopbits 1

line aux 0

exec-timeout 30 0

password 7 0307585A025E701C18

logging synchronous

modem InOut

modem autoconfigure discovery

transport input all

stopbits 1

flowcontrol hardware

line vty 0 4

exec-timeout 30 0

password 7 1511085D007B7A747E

transport input ssh

!

ntp authenticate

ntp clock-period 17180144

ntp server x.x.64.8

!

webvpn cef

!

end

ClarkCounty#