Current configuration : 2177 bytes

!

version 12.4

service timestamps debug datetime msec

service timestamps log datetime msec

no service password-encryption

!

hostname Router

!

boot-start-marker

boot-end-marker

!

card type e1 1

!

no aaa new-model

!

resource policy

!

network-clock-participate E1 1/0

network-clock-participate E1 1/1

ip subnet-zero

!

isdn switch-type primary-qsig

!

voice-card 0

!

voice service voip

sip

bind control source-interface FastEthernet0/0

bind media source-interface FastEthernet0/0

!

voice class codec 1

codec preference 1 g729r8

codec preference 2 g711ulaw

codec preference 3 g711alaw

!

controller E1 1/0

clock source internal

pri-group timeslots 1-31

!

controller E1 1/1

!

interface FastEthernet0/0

ip address A.B.C.D 255.255.255.0

duplex auto

speed auto

interface FastEthernet0/1

no ip address

shutdown

duplex auto

speed auto

!

interface Serial1/0:15

no ip address

encapsulation hdlc

isdn switch-type primary-qsig

isdn overlap-receiving

isdn protocol-emulate network

isdn incoming-voice voice

no cdp enable

!

ip http server

!

ip classless

ip route 0.0.0.0 0.0.0.0 A.B.C.B

!

control-plane

!

voice-port 1/0:15

!

dial-peer voice 1 voip

destination-pattern .T

voice-class codec 1

session protocol sipv2

session target dns:domain.com:5060

dtmf-relay rtp-nte digit-drop

!

!

dial-peer voice 11111 pots

destination-pattern 11111

direct-inward-dial

port 1/0:15

forward-digits all

authentication username 11111@domain.com password xxxx realm domain.com

!

dial-peer voice 11112 pots

destination-pattern 11112

direct-inward-dial

port 1/0:15

forward-digits all

authentication username 11112@domain.com password xxxx realm domain.com

!

dial-peer voice 11113 pots

!	!	!	!

!	!	!	!

!	!	!	!

!	!	!	!

sip-ua

no remote-party-id

retry invite 3

retry notify 3

timers notify 100

registrar dns:domain.com:5060 expires 3600

sip-server dns:domain.com:5060

!