(I can't reach from branch8 new router to branch1 router)

Head Office Router

interface Loopback0

ip address 172.30.100.1 255.255.255.0

!

interface Tunnel0

description ** Multipoint GRE Tunnel **

bandwidth 4000

ip address 10.205.0.1 255.255.255.0

no ip redirects

ip mtu 1436

ip nhrp authentication dmgre

ip nhrp map multicast dynamic

ip nhrp network-id 1

ip nhrp holdtime 3600

ip ospf message-digest-key 1 md5 7 070C285F4D064E5204

ip ospf network broadcast

ip ospf priority 2

tunnel source FastEthernet0/1

tunnel mode gre multipoint

tunnel key 1

!

interface FastEthernet0/0

description ** LAN Segment **

ip address 10.199.99.11 255.255.255.0

no ip redirects

ip ospf message-digest-key 1 md5 7 00071A1507545C5158

speed 100

full-duplex

no standby redirect

standby 1 ip 10.199.99.10

standby 1 priority 150

standby 1 preempt

!

interface FastEthernet0/1

description ** ADSL MegaPOP 2M WAN Link LclDel#  **

ip address xxx.xxx.xxx.xxx 255.255.255.252

speed 100

full-duplex

!

router ospf 1

log-adjacency-changes

area 0 authentication message-digest

area 1 authentication message-digest

area 1 range 10.200.0.0 255.255.128.0

area 1 range 10.205.1.0 255.255.255.192

redistribute static metric 500 metric-type 1 subnets route-map filterstatic

network 10.199.99.0 0.0.0.255 area 0

network 10.205.0.0 0.0.0.255 area 1

network 10.205.2.0 0.0.0.255 area 1

network 10.205.3.0 0.0.0.255 area 1

default-information originate

!

ip classless

ip route 0.0.0.0 0.0.0.0 10.199.99.21

Branch 1 (IOS 12.2(15)T10)

ip cef

!

isdn switch-type basic-net3

!

!

!

interface Loopback0

ip address 172.30.1.1 255.255.255.0

!

interface Tunnel0

description ** Dynamic GRE Tunnel **

bandwidth 2000

ip address 10.205.0.2 255.255.255.0

no ip redirects

ip mtu 1436

ip nhrp authentication dmgre

ip nhrp map 10.205.0.1 xxx.xxx.xxx.xxx

ip nhrp map multicast xxx.xxx.xxx.xxx

ip nhrp network-id 1

ip nhrp holdtime 3600

ip nhrp nhs 10.205.0.1

ip ospf message-digest-key 1 md5 7 00071A1507545C5158

ip ospf network broadcast

ip ospf priority 0

tunnel source ATM0.1

tunnel mode gre multipoint

tunnel key 1

!

interface ATM0

bandwidth 2000

no ip address

no atm ilmi-keepalive

dsl operating-mode auto

!

interface ATM0.1 point-to-point

description ** ADSL MegaPOP 2M WAN Link LclDel# **

mtu 1500

bandwidth 2000

ip address xxx.xxx.xxx.xxx 255.255.255.252

pvc 8/35

encapsulation aal5snap

!

!

interface BRI0

no ip address

encapsulation ppp

dialer pool-member 1

isdn switch-type basic-net3

ppp authentication chap

!

interface FastEthernet0

description ** LAN Segment **

ip address 10.200.1.1 255.255.255.0

ip ospf message-digest-key 1 md5 7 110A1016141D5C5B53

speed auto

!

interface Dialer0

description ** ISDN Backup **

bandwidth 64

ip address 10.205.2.2 255.255.255.252

encapsulation ppp

ip ospf message-digest-key 1 md5 7 13061E010803537D7C

ip ospf hello-interval 30

dialer pool 1

dialer remote-name xxxx

dialer idle-timeout 10

dialer string xxxxxxxx

dialer string xxxxxxxx

dialer watch-group 1

dialer-group 1

ppp authentication chap

!

router ospf 1

log-adjacency-changes

area 1 authentication message-digest

passive-interface FastEthernet0

network 10.0.0.0 0.255.255.255 area 1

!

ip classless

Branch 2 (1721 Router IOS12.2(4)YA2)

isdn switch-type basic-net3

!

buffers middle permanent 60

buffers middle max-free 300

buffers middle min-free 30

!

!

interface Loopback0

ip address 172.30.2.1 255.255.255.0

!

interface Tunnel0

description ** Dynamic GRE Tunnel **

bandwidth 2000

ip address 10.205.0.3 255.255.255.0

no ip redirects

ip mtu 1436

ip nhrp authentication dmgre

ip nhrp map 10.205.0.1 xxx.xxx.xxx.xxx

ip nhrp map multicast xxx.xxx.xxx.xxx

ip nhrp network-id 1

ip nhrp holdtime 3600

ip nhrp nhs 10.205.0.1

ip ospf message-digest-key 1 md5 7 02050D4808095876B1

ip ospf network broadcast

ip ospf priority 0

no keepalive

tunnel source ATM0.1

tunnel mode gre multipoint

tunnel key 1

!

interface ATM0

bandwidth 2000

no ip address

no atm ilmi-keepalive

dsl operating-mode auto

!

interface ATM0.1 point-to-point

description ** MegaPOP 2M WAN Link LclDel # **

mtu 1500

bandwidth 2000

ip address xxx.xxx.xxx.xxx 255.255.255.252

pvc 8/35

encapsulation aal5snap

!

!

interface BRI0

no ip address

encapsulation ppp

dialer pool-member 1

isdn switch-type basic-net3

ppp authentication chap

!

interface FastEthernet0

description ** LAN **

ip address 10.200.2.1 255.255.255.0

ip ospf message-digest-key 1 md5 7 01100F175804515876

speed auto

!

interface Dialer0

description ISDN Backup to

bandwidth 64

ip address 10.205.2.6 255.255.255.252

encapsulation ppp

ip ospf message-digest-key 1 md5 7 110A1016141D5C5B35

ip ospf hello-interval 30

dialer pool 1

dialer remote-name xxxxxx

dialer idle-timeout 10

dialer string xxxxxxxxxx

dialer string xxxxxxxxxx

dialer watch-group 1

dialer-group 1

ppp authentication chap

!

router ospf 1

log-adjacency-changes

area 1 authentication message-digest

network 10.0.0.0 0.255.255.255 area 1

!

ip classless

Branch 3 (1721 Router IOS12.2(4)YA2)

isdn switch-type basic-net3

!

!

!

interface Loopback0

ip address 172.30.3.1 255.255.255.0

!

interface Tunnel0

description ** Dynamic GRE Tunnel **

bandwidth 2000

ip address 10.205.0.4 255.255.255.0

no ip redirects

ip mtu 1436

ip nhrp authentication dmgre

ip nhrp map 10.205.0.1 xxx.xxx.xxx.xxx

ip nhrp map multicast xxx.xxx.xxx.xxx

ip nhrp network-id 1

ip nhrp holdtime 3600

ip nhrp nhs 10.205.0.1

ip ospf message-digest-key 1 md5 7 00071A1507545C5185

ip ospf network broadcast

ip ospf priority 0

no keepalive

tunnel source ATM0.1

tunnel mode gre multipoint

tunnel key 1

!

interface ATM0

bandwidth 2000

no ip address

no atm ilmi-keepalive

dsl operating-mode auto

!

interface ATM0.1 point-to-point

description ** MegaPOP 2M WAN Link LclDel# **

mtu 1500

bandwidth 2000

ip address xxx.xxx.xxx.xxx 255.255.255.252

pvc 8/35

encapsulation aal5snap

!

!

interface BRI0

no ip address

encapsulation ppp

dialer pool-member 1

isdn switch-type basic-net3

ppp authentication chap

!

interface FastEthernet0

description ** LAN Segment **

ip address 10.200.3.1 255.255.255.0

ip ospf message-digest-key 1 md5 7 045802150C2E1B19E5

speed auto

!

interface Dialer0

description ** ISDN Backup **

bandwidth 64

ip address 10.205.2.10 255.255.255.252

encapsulation ppp

ip ospf message-digest-key 1 md5 7 01100F175804515867

ip ospf hello-interval 30

dialer pool 1

dialer remote-name xxxx

dialer idle-timeout 10

dialer string xxxxxxxx

dialer string xxxxxxxx

dialer watch-group 1

dialer-group 1

ppp authentication chap

!

router ospf 1

log-adjacency-changes

area 1 authentication message-digest

passive-interface FastEthernet0

network 10.0.0.0 0.255.255.255 area 1

!

ip classless

Branch 8 (1721 Router IOS 12.2(4)YA2)

isdn switch-type basic-net3

!

!

!

interface Loopback0

ip address 172.30.8.1 255.255.255.0

!

interface Tunnel0

description ** Dynamic GRE Tunnel **

bandwidth 2000

ip address 10.205.0.8 255.255.255.0

no ip redirects

ip mtu 1436

ip nhrp authentication dmgre

ip nhrp map 10.205.0.1 xxx.xxx.xxx.xxx

ip nhrp map multicast xxx.xxx.xxx.xxx

ip nhrp network-id 1

ip nhrp holdtime 3600

ip nhrp nhs 10.205.0.1

ip ospf message-digest-key 1 md5 7 02050D4808095876B1

ip ospf network broadcast

ip ospf priority 0

no keepalive

tunnel source ATM0.1

tunnel mode gre multipoint

tunnel key 1

!

interface ATM0

bandwidth 2000

no ip address

no atm ilmi-keepalive

bundle-enable

dsl operating-mode auto

hold-queue 224 in

!

interface ATM0.1 point-to-point

description ** SingTel ADSL MegaPOP 2M WAN Link LclDel# **

mtu 1500

bandwidth 2000

ip address xxx.xxx.xxx.xxx 255.255.255.252

pvc 8/35

encapsulation aal5snap

!

!

interface BRI0

no ip address

encapsulation ppp

dialer pool-member 1

isdn switch-type basic-net3

ppp authentication chap

!

interface FastEthernet0

description ** LAN Segment **

ip address 10.200.8.1 255.255.255.0

ip ospf message-digest-key 1 md5 7 094F471A1A0A4045C5

ip policy route-map clear-df

speed auto

!

interface Dialer0

description ** ISDN Backup **

bandwidth 64

ip address 10.205.2.26 255.255.255.252

encapsulation ppp

ip ospf message-digest-key 1 md5 7 1511021F07257C73F7

ip ospf hello-interval 30

dialer pool 1

dialer remote-name xxxxx

dialer idle-timeout 10

dialer string xxxxxxxx

dialer string xxxxxxxx

dialer watch-group 1

dialer-group 1

ppp authentication chap

!

router ospf 1

log-adjacency-changes

area 1 authentication message-digest

passive-interface FastEthernet0

network 10.0.0.0 0.255.255.255 area 1

!

ip classless

Branch 8 New Router (1841 IOS 12.4)

ip cef

!

!

!

!

no ip domain lookup

ip domain name xxxx.xxx.xxx

ip host c1 xxxx.xxx.xxx

ip host c2 xxxx.xxx.xxx

isdn switch-type basic-net3

!

username xxxxx password 7 xxxxxxxxxxx

!

!

!

interface Tunnel0

description ** Dynamic GRE Tunnel **

bandwidth 2000

ip address 10.205.0.8 255.255.255.0

no ip redirects

ip mtu 1436

ip nhrp authentication dmgre

ip nhrp map 10.205.0.1 xxxx.xxx.xxx

ip nhrp map multicast xxxx.xxx.xxx

ip nhrp network-id 1

ip nhrp holdtime 3600

ip nhrp nhs 10.205.0.1

ip ospf message-digest-key 1 md5 7 02050D4808095876B1

ip ospf network broadcast

ip ospf priority 0

tunnel source ATM0/0/0.1

tunnel mode gre multipoint

tunnel key 1

!

interface Loopback0

ip address 172.30.8.1 255.255.255.0

!

interface FastEthernet0/0

description ** LAN Segment**

ip address 10.200.8.1 255.255.255.0

ip policy route-map clear-df

ip ospf message-digest-key 1 md5 7 094F471A1A0A4045C5

duplex auto

speed auto

!

interface FastEthernet0/1

no ip address

shutdown

duplex auto

speed auto

!

interface ATM0/0/0

bandwidth 2000

no ip address

no atm ilmi-keepalive

bundle-enable

dsl operating-mode auto

hold-queue 224 in

!

interface ATM0/0/0.1 point-to-point

description ** MegaPOP 2M WAN Link LclDel# **

mtu 1500

bandwidth 2000

ip address xxxx.xxx.xxx 255.255.255.252

pvc 8/35

encapsulation aal5snap

!

!

interface BRI0/1/0

no ip address

encapsulation ppp

dialer pool-member 1

isdn switch-type basic-net3

isdn point-to-point-setup

ppp authentication chap

!

interface Dialer0

description ** ISDN Backup **

bandwidth 64

ip address 10.205.2.26 255.255.255.252

encapsulation ppp

ip ospf message-digest-key 1 md5 7 1511021F07257C737F

ip ospf hello-interval 30

dialer pool 1

dialer remote-name xxxxx

dialer idle-timeout 10

dialer string xxxxxxx

dialer string xxxxxxx

dialer watch-group 1

dialer-group 1

ppp authentication chap

!

router ospf 1

log-adjacency-changes

area 1 authentication message-digest

passive-interface FastEthernet0/0

network 10.0.0.0 0.255.255.255 area 1

!

ip classless