AFTER MULTILINK

CHI-WAN-2

!

interface Multilink10

ip address 10.250.254.153 255.255.255.252

ppp multilink

multilink-group 10

!

interface Serial0/0/0:0

description *** Chicago to Orlando (MCI CKT ID's - MGBHXWRK0001) ***

bandwidth 1536

no ip address

service-policy output DownersGrove_OUT

encapsulation ppp

no ip mroute-cache

no fair-queue

serial restart_delay 0

ppp multilink

multilink-group 10

ip route-cache flow

ip rtp header-compression

ip rtp compression-connections 254

!

interface Serial0/0/1:0

description *** Chicago to Orlando (MCI CKT ID's - MGBH34PG0001) ***

bandwidth 1536

no ip address

service-policy output DownersGrove_OUT

encapsulation ppp

no ip mroute-cache

no fair-queue

serial restart_delay 0

ppp multilink

multilink-group 10

ip route-cache flow

ip rtp header-compression

ip rtp compression-connections 254

!

ORL-WAN-2

!

interface Multilink10

ip address 10.250.254.154 255.255.255.252

ppp multilink

multilink-group 10

!

interface Serial6/0:0

description *** T1 to Downers Grove-Chicago (MCI CKT ID's - MGBHXWRK0001) ***

bandwidth 1536

no ip address

service-policy output DownersGrove_OUT

encapsulation ppp

no ip mroute-cache

no fair-queue

serial restart_delay 0

ppp multilink

multilink-group 10

ip rtp header-compression

ip rtp compression-connections 254

!

interface Serial6/1:0

description *** T1 to Downers Grove-Chicago (MCI CKT ID's - MGBH34PG0001) ***

bandwidth 1536

no ip address

service-policy output DownersGrove_OUT

encapsulation ppp

no ip mroute-cache

no fair-queue

serial restart_delay 0

ppp multilink

multilink-group 10

ip rtp header-compression

ip rtp compression-connections 254

!